## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Young Ik Jo
Status Report for RAN WG3
3GPP TSG RAN #98, Electronic Meeting
Dec 12th – 16th, 2022
RP-222696

## Slide 2: Executive Summary
Total 1191 Tdocs at submission deadline (excluding LSin received from other groups) in Q4
  6% LSs and related documents
  24% Maintenance: Rel-17 & earlier
  61% Documents to Rel-18 WIs/SIs
Updated endorsed guidelines for e-meeting: R3-225343
Endorsed guidelines for f2f meeting with remote access: R3-226188
The R18 NR Positioning SI (led by RAN1) and the R18 Network Energy Savings SI(led by RAN1) were completed in RAN3.
The rules on references to RRC specifications (e.g. TS 38.331) was agreed in R3-226777 and captured in TR30.531.
A special contribution was submitted in R3-226918 and approved:)
RAN3#117bis-e | Oct 10th – 18th, 2022
RAN3#118 | Nov 14th – 18th, 2022 Toulouse, France
RAN #98e | Dec 12th – 16th, 2022

## Slide 3: Tdoc submitted to RAN3
The total number of contributions around 900 for each RAN3 meeting is affordable
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: Tdocs for each Topic

## Slide 6: Overview of RAN3-led Rel-18 NR SI/WIs
UID | Name (acronym) | Acronym | Target completion | Old % (the same as in WI/SI SR) | WID | New % | Change or comments
941009 | Mobile IAB (Integrated Access and Backhaul) for NR WI | NR_mobile_IAB | 23/12/2023 | 5% | WID: RP-222671 | 20% | The reply LS to SA2 on FS_VMR solutions was agreed in R3-226048 and cc RAN
941008 | Enhancement on NR QoE management and optimizations for diverse services WI | NR_QoE_enh | 23/12/2023 | 10% | WID: RP-221803 | 30% | 
941010 | Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN WI | NR_AIML_NGRAN | 23/06/2023 | 10% | WID: RP-220635 | 30% | 
941007 | Further enhancement of data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) WI | NR_ENDC_SON_MDT_enh2 | 23/12/2023 | 10% | WID: RP-221825 | 30% | 
940088 | Enhancement for resiliency of gNB-CU-CP SI | FS_gNB_CU_CP_resiliency | 22/09/2022 | 100% | SID: RP-221438 SR: RP-222250 |  | 
WI: Black SI: Blue Completed WI/SI: Red

## Slide 7: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-222697, which includes:
  73 CRs were agreed in Q4.
  12 Rel-16 Cat.F CRs
  61 Rel-17 CRs: 12 Cat.A CRs, 49 Cat.F CRs
    1 Cat.F in R3-226832 Clarification of the desired buffer size in case of retransmissions [DesBufRetrans]
  9 Non-Backwards-Compatible (NBC) CRs for Rel-17
    R3-226113, R3-226115, R3-226120, R3-226238, R3-226239, R3-226333, R3-226845, R3-226845, R3-226789
    (Here is how 3GPP works with NBC changes)
  14 endorsed draftCRs to RAN2 specs.

## Slide 8: Statistics for GTW Usage
Overall, roughly 23 hours of GTW conference calls in RAN3#117bis-e
Statistics shown below
  TEI/LS items were handled via online and email discussions (3 hour of GTW time used)
  And remaining 20 hours of GTW conference call time was used for Rel-18 items
  GTW conference call time was mainly used for R18 WI/SIs, only part of TEI corrections topics were open for Oct meeting.

## Slide 9: Experience for GTW Usage in f2f meeting
RAN3 had one meeting room for main session, the other one is breakout room for offline discussion shared with RAN2 (WGs secretaries maintain the time schedule table and it works well, thanks YoungIK and Juha), and booked two parallel GTW sessions for two meeting rooms for entire meeting duration.
The voice quality in general is good, but only one microphone in the main room for comments, the meeting was interrupted twice due to the microphone issue.
The audio device test for remote access need to be performed before daily session starts.
MCC and IT support during the meeting is sufficient.
Overall, RAN3#118 was a successful F2F meeting with remote access!

## Slide 10: R18 SON/MDT WI
Progress in the last quarter
For SHR and SPCR:
  T310 and T312 related triggers are to be considered for inter-RAT SHR from NR to LTE.RAN3 provides parameters can be useful for optimizing inter-RAT successful handover from NR to LTE and LS RAN2 to confirm and request support. Whether the existing IEs defined in Rel-17 for intra-NR SHR can be reused is up to RAN2 decision.
  RAN3 provides parameter information can be included as part of SPCR (parallel discussion happening in RAN2 as well, no need to LS RAN2 if already agreed in RAN2).T310 of SCG and T312 of SCG are not considered as SPCR triggers for classic PSCell addition or CPA.SPR as abbreviation for Successful PScell Change Report feature. For SN-initiated classic PScell change the source SN node decides the T310/T312 triggers (e.g timer threshold) and the target SN node decides the T304 triggers (e.g timer threshold).
For MRO:
  CPA Execution to wrong PSCell will be considered, e.g. UE receives CPA configuration and CPA execution condition is satisfied, CPA execution fails or an SCG failure occurs shortly after a successful CPA execution; a suitable PSCell different with target PSCell is found based on the measurements reported from the UE.Too Early CPA Execution will be considered.
  It is beneficial for the UE to report at least the cause of the fast MCG recovery failure (at least T316 expiry, SCG failure) and also, if the problem is SCG failure, the SCG failure type (at least t310-Expiry, randomAccessProblem, rlc-MaxNumRetx).
  Too Late CPC Execution, Too Early CPC Execution and CPC Execution to wrong PSCell will be considered.
  For MRO for CPAC, deprioritize Case i/ii/iii/iv.
  For MRO for MR-DC SCG failure, deprioritize dual failure case (i.e. both MCG failure and SCG failure occur).
  MRO for inter-system handover for voice fallback:Deprioritize Case 5,Deprioritize MRO enhancements for redirection for voice fallback,Introduce stage 2 descriptions of failure type definition for inter-system inter-RAT HO from NR to E-UTRA for voice fallback.The RLF Report needs to indicate that the last failed inter-system inter-RAT HO was triggered due to voice fallback.
For RACH enhancement:
  RA report is enhanced to include feature combination related information.
  RACH report retrieval: a)WA: RAN3 works on the network based solution for RACH report retrieval, i.e., gNB-DU indicates to gNB-CU about RACH occurrence;b)WA: SN should indicate the potential availability of RA report to the MN, MN can fetch the RA report and transfer it to SN;c)Send LS to RAN2 with RAN3 assumption and ask RAN2 to provide feedback on UE based solution
  RAN3 supports a network-based solution for RACH report retrieval over F1AP based on an indication from the gNB-DU to the gNB-CU of successful RACH procedures which are not known to the gNB-CU (e.g., when RACH is triggered due to beam failure recovery, no PUCCH resource available, UL sync issue)
  Define a new class-2 F1AP message (e.g., RACH INDICATION) to indicate certain RACH occurrence(s) from gNB-DU to gNB-CU.

## Slide 11: R18 SON/MDT WI
Progress in the last quarter
For SON/MDT Enhancements for Non-Public Networks:
  RAN3 sends an LS to SA3 (cc SA5, RAN2) for user consent of NPN including the following aspects:
  1: For PNI-NPN, whether existing user consent for management-based MDT (i.e., Management Based MDT PLMN List IE) can also apply for MDT in PNI-NPNs (no need of CAG-ID in user consent).
  2: For SNPN, whether user consent for SNPN should include a list of SNPNs (PLMNs + NIDs) where management based MDT is allowed to take place.
  Introduce a CAG list for MDT area scope.
  The use cases RAN3 should support are:
  Use Case 1: Enhanced area scope information should allow collection of MDT measurements in specific PNI-NPNs, i.e. MDT measurements should be collected only within specific CAGs.
  Use Case 2: Enhanced area scope information should allow collection of MDT measurements both in specific PNI-NPNs (i.e. in specific CAGs) and in public network areas (e.g. specific PN cells, TAIs, etc.).
  Agree to the addition of a CAG list inside and outside the current choice structure for the MDT Area Scop).
For SON for NR-U:
  For XnAP, add in the RESOURCE STATUS UPDATE message a Channel Occupancy Time Percentage UL IE and an Energy Detection Threshold UL IE as sub-IEs of NR-U Channel Item IE. Corresponding TP is in R3-226040.
  Rename the existing Channel occupancy time percentage DL IE as Channel Occupancy Time Percentage DL both in F1AP and XnAP from R17..
For MDT enhancement:
  It is RAN3’s understanding that the Rel-17 feature of signaling based logged MDT override protection applies only during Intra-NR reselection and applies to Intra-5GS (gNB–>gNB).
  Whether to support cross-RAT logged MDT reporting (i.e., whether the NR node needs to retrieve LTE logged MDT report) for signaling based logged MDT override protection is pending on RAN2 progress.
  Wait for RAN2’s progress on cross-RAT logged MDT reporting before discussing whether any enhancements are needed for NG-RAN to forward the LTE logged MDT reports to the correct TCE.

## Slide 12: R18 SON/MDT WI
Next steps
Further discuss UE context retrieval for both inter-RAT SHR and intra-RAT SHR and the objective of SPCR.
Further discuss what information should be included/not included in the Successful PSCell Change Report.
Further discuss How to forward the SCG failure information from the MN to the SN for NE-DC and (NG) EN-DC scenarios.
Further discuss other information needed in RA report.
Further check the detail of solution over F1 for RA report.
Postpone discussions on inclusion of SNPN identifiers in MDT area scope to next meeting.

## Slide 13: R18 QoE WI
Progress in the last quarter
Whether UE can only report the INACTIVE/IDLE QoE reports to gNB when UE has entered RRC_CONNECTED due to other reasons is pending to RAN2.
RAN3 discuss the alignment between logged MDT and MBS QoE when basic solution for MBS QoE has been defined first.
OAM should have the flexibility to collect QoE only in high mobility and/or in HSDN cell.
Use the same set of parameters in QMC configuration for all RRC states.
In case of management-based QoE, the MN decides which node to perform the QoE measurement configuration.
The MN can generate an RVQoE configuration for a UE. The SN can generate an RVQoE configuration for a UE.
UE can send RVQoE report to the MN, the MN then forward the RVQoE report to the SN if needed, and vice versa.
QoS flow ID(s) should be included in the RAN visible QoE report collected at the UE.
DRB ID(s) should be transmitted over F1 as the QoS flow information in the RVQoE report.
RAN3 checks with SA4 on whether RVQoE value can reflect the overall situation of the experience of an ongoing service, with multiple QoE metrics taken into account, not limited to only RVQoE metrics.
Introduce buffer level as a threshold-based trigger for RVQoE reporting.
Impacts and dependencies on other WGs
UE behaviour is pending to progress in RAN2
Further discuss left-over issues of R17, taking into account futher input from SA4.
Next steps
Further discuss whether any enhancements are needed for high speed scenario.
Further discuss whether UE-based or CN-based solution shall be selected for IDLE QoE.
Further discuss the configuration and reporting of QoE/RVQoE in NR-DC
Continue to work on stage2 and stage3.

## Slide 14: R18 AI RAN WI
Progress in the last quarter
Procedures used for AI/ML support in the NG-RAN shall be use case agnostic.
WA: Procedures used for AI/ML support in the NG-RAN shall be “data type agnostic”.
Legacy information that are used to support AI/ML are transferred via existing legacy procedures (no need to signal them via other procedures)
WA: Solutions for AI/ML information exchange over the NG interface are not considered as part of Rel18.
Introduce a new Class 1 procedure for initiating the reporting of AI/ML Related Information and a Class 2 procedure for Data Reporting of AI/ML Related Information. The new procedure is non-UE associated procedure.
Cell-based UE Trajectory prediction has the same structure as UE History Information IE. Cell-based UE Trajectory prediction is provided as a list of cells into the future, each of which is indicated together with an expected time of stay into the cell.
The request/response in the new Class 1 procedure for initiating the reporting of AI/ML Related Information can include an ID assigned by the requesting/responsing NG-RAN node. UE Trajectory Prediction is transferred to the target gNB via the Handover Request.
UE Trajectory Prediction is transferred to the target gNB via the Handover Request.
The "Energy Efficiency" metric should be measurable, produced and interpretable by the RAN.
WA: Take the EE defined in SA5 as the baseline for the energy efficiency of a gNB.
Next steps
Continue to work on stage2 and stage3.

## Slide 15: R18 mobile IAB WI
Progress in the last quarter
The reply LS to SA2 on FS_VMR solutions was agreed in R3-226048.
mIAB-DU migration and mIAB-MT handover can be executed independently from each other. Details on the scenarios need to be further discussed.
WA: The mIAB-MT and its co-located mIAB-DU can be handed over/migrated to different donor CUs. This WA is subject to validation that the impact involved is affordable.
The source donor CU for the mIAB-MT HO provides to the donor CU serving the mIAB-DU at least the: gNB ID of the target donor CU for the mIAB-MT HO; ID(s) of the mIAB-MT, this info can be sent after the completion of IAB-MT HO.
In case the donor of the mIAB-DU decides the F1AP setup for DU migration, the donor of the mIAB-DU triggers via F1 signalling the IAB node to perform the F1 Setup procedure for the DU migration. An OAM based solution is not excluded.
Focus first on the scenarios where Xn and IP connectivity are available between the source and target donors for IAB-MT HO and mIAB-DU migration.
PCI-change on the IAB-node can be supported via handover of connected UEs between cells using old and new PCI, respectively. PCI collision can be detected by the F1-terminating IAB-donor of the mobile IAB-node.
Static TAC solution is not pursued. RAN3 assumes that dynamic TAC solution should be supported.
Next steps
Continue to work on stage2 and stage3.

## Slide 16: R18 Mobility Enh. WI
Progress in the last quarter
For L1/L2-triggered mobility, the high-level signalling procedures for both intra-DU and inter-DU cases are designed.
RAN3 works on the same signaling procedure for both initial cell switch and subsequent cell switch for intra-DU L1/L2-triggered mobility.
A reply LS R3-226829 regarding L1/L2-triggered mobility is agreed to be sent out to RAN1, RAN2 and RAN4.
Direct data forwarding is supported by current specification, FFS on further signaling enhancement. Optimization on indirect data forwarding is by network implementation.
RAN3 acknowledges unnecessary signaling exchange between MN and the target SN would cause inefficiency and extra latency for CHO + NR-DC, the solution is FFS.
The issue on new problem of CHO with multiple SCGs at the target side is FFS.
WA: In CHO with (multiple) SCG configuration, the (candidate) SN can acknowledge whether it has direct data forwarding path with source SN. If existed, it can assign the same data forwarding address for multiple data forwarding paths, otherwise, it is up to the candidate SN implementation.
Impacts and dependencies on other WGs
More RAN2 input is expected and helpful.
Next steps
Continue to work on stage2 and stage3.

## Slide 17: R18 MBS WI
Progress in the last quarter
Coordination among WG (SA2/RAN2/RAN3) on network sharing solutions;
Principle identified for network sharing (e.g., backward compatibility; dynamics in network sharing for MOCN; MB-SMF/AF/MBSF is not aware which NG-RAN node or which cell within a NG-RAN node is shared);
How RAN handles different info from 5GC in case of MOCN (e.g., It is up to the NG-RAN node implementation on how to handle different QoS parameters for the same service from different PLMNs in case different QoS parameters for the same service are received);
Network sharing for MBS in case of local MBS service and location dependent MBS service;
NG-U options in case of MOCN;
F1AP options in case of MOCN and multiple cell-ID broadcast.
Impacts and dependencies on other WGs
Wait for SA2 on solution down-selection for network sharing for MBS broadcast.
Next steps
Further study on how to handle different area session IDs allocated from different PLMNs, whether and how to handle different service areas associated with the area session IDs, in case of network sharing for MBS;
Further study how many NG-U tunnels to be set up in case of MOCN;
Further study single or multiple F1AP signaling in case of MOCN;
Per multicast session level or per UE level from 5GC is needed?
Further study RRC_INACTIVE support in RAN3 based on latest RAN2 progress on PTM config delivery.

## Slide 18: R18 Sidelink Relay WI
Progress in the last quarter
RAN3 reply SA2’s LS on authorization for U2U relay that RAN3 currently considers that there is no need to provide the authorization information for UE-to-UE Relay operation to the NG-RAN. But RAN3 could enhance the "5G ProSe authorised" information, if needed, based on the RAN2’s progress.
Source gNB selects the target path type (direct or indirect). For direct/indirect to indirect path switching, enhance Xn: HANDOVER REQUEST to include at least the Remote UE L2 ID and Relay UE L2 ID. FFS whether to include a single Target Relay L2 ID or a list of Target candidate Relay L2 IDs.
For the multi-path support, the gNB-CU takes the responsibility to decide the addition/ modification/release of the path. For intra-DU and inter-DU cases, the UE Context Setup / Modification procedure can be reused to configure the 2nd path with possible enhancements. The details will be discussed based on RAN2 progress.
The gNB-CU is responsible to determine the data split among two paths for a DRB for both intra-DU and inter-DU cases. For intra-DU case, two F1-U tunnels are setup between CU and DU for a split DRB. FFS on how to support the multi-path delivery of split SRB. WA: For inter-DU case, legacy DC based data split/duplication mechanism can be reused as baseline for split DRB/SRB.
WA: The direct path and indirect path cannot be configured for a remote UE simultaneously in this release, depending on RAN2 decision.
For Scenario 2, interface between UEs are non-3GPP defined. Therefore in the UE context setup/modification procedure, the PC5 Relay RLC channel configurations are not needed for remote UE and relay UE.
Other important info
From RAN3 point of view, the Multi-path study phase is completed, and the Multi-path can move to normative work phase.
Next steps
Continue to discuss authorization and service continuity.
Normaltive work for multi-path support.

## Slide 19: R18 NR NTN WI
Progress in the last quarter
Mobility and Service Continuity Enhancements
- There is no need to exchange the cell coverage stop time in the signaling if the time-based CHO parameters.
- Agree to add time information for time-based CHO, which includes as a start time T1 and time duration T2, in Xn Handover Request message.
- There is no need to exchange a ‘Hard or Soft Feeder Link Switch over indication’ via Xn Setup procedure and Configuration Update procedure.
- WA: Uu Cell ID is used in HO signalling.
- The earth moving cell (EMC) scenario described in Section 3.1 of R3-226859 is valid.
Network verified UE location
- RAN3 is not affected by UE location reporting.
- No additional RAN3 impact if UE location is not correct.
Next steps
Further discuss what’s the TAC to be used when using Uu cell ID in Xn setup and configuration update procedure.
How to support this EMC case?
Any other impacts, in addition to the support for transferring {T1, duration} over NGAP?
Other issues if any

## Slide 20: R18 IoT NTN WI
Progress in the last quarter
The new cause value “Release due to discontinuous coverage” is applicable for the UE Context Release Request procedure.
Add stage 2 description on the behavior of eNB when it detects the UE is out of coverage.
Impacts and dependencies on other WGs
Further discuss the potential RAN3 impact based on the progress in SA2.
Next steps
Align with the progress in NR NTN WI.

## Slide 21: R18 UAV WI
Progress in the last quarter
Agreed to introduce Aerial UE Subscription Information IE over NGAP in INITIAL CONTEXT SETUP, UE CONTEXT MODIFICATION, HANDOVER REQUEST, PATH SWITCH REQUEST ACKNOWLEDGE messages.
The Aerial UE Subscription Information IE is based on LTE format with codepoints ENUMERATED (allowed, not allowed, …)
Introduce Aerial UE Subscription Information IE over XnAP.
RAN3 will not initiate the discussion on Inter-RAT and NR-DC support.
Impacts and dependencies on other WGs
Whether additional codepoints are needed for Aerial UAV Subscription Information IE is subject to SA2 and RAN2 discussions.
Next steps
Further discussion on NR support for UAV may be triggered by other WGs.

## Slide 22: R18 NR NCR SI
Progress in the last quarter
The NCR authorization indicator is provided from AMF to gNB explicitly.
gNB-CU knows whether the connected gNB-DU supports NCR based on OAM configuration.
gNB-DU needs to know the authorization status of NCR.
OAM-NCR connectivity can be provided via PDU session.
Exclude the solution 2.
Take solution 3 as the basis for NCR management. FFS on any additional aspects.
Next steps
Whether NCR may be configured with a list of allowed and/or forbidden cells.
Discussion on further stage 2 related aspects agreed by RAN1.
Whether the needs for gNB-CU or gNB-DU to configure which cell(s) can be used for NCR device accessing.

## Slide 23: R18 NR Positioning SI
Progress in the last quarter
RAN3 will align with RAN1/RAN2 decisions on terminologies for Ranging/Sidelink positioning.
Send LS to other involved groups about RAN3’s agreements and progress.
Other important info
This R18 positioning SI is completed in RAN3.

## Slide 24: R18 NR Network ES SI
Progress in the last quarter
Agree the TP on beam level activation.
No need to capture in TR about the cell DTX/DRX information and the joint or separate DTX and DRX configuration.
On the exchange NES state over network interfaces, RAN3 can further work pending on other group decision at normative phase.
No consensus on the TP on the increased autonomy for gNB-DU. RAN3 can further work on the increased autonomy for gNB-DU pending on development of other NES techniques at normative phase.
Agree a simple TP on the paging enhancement.
Other important info
This R18 Network Energy Saving SI is completed in RAN3.

## Slide 25: TEI Corrections
Progress in the last quarter
R17 MBS corrections:
  Various LS addressed/noted; Various corrections to NG/F1/E1/Xn interface (e.g., User Inactivity for Multicast Session; name and semantics; F1-U references to UE Context; F1-U tunnels; E1AP protocol Error enabling Multicast Bearer Context Setup w/o MRB configuration available, etc.) and stage 2/message flow corrections (e.g., 38.300, 38.401); Various ASN.1 corrections.
  Delay issue for the CU-CP to configure the multicastHFN-AndRefSN IE to the UE, wait for RAN2 feedback based on the latest RAN3 LS; PDCP wrap-around issue.
R17 Positioning corrections:
  A new procedure is used for support of positioning system information over F1AP.
  Add the values sl128, sl256, sl512, and sl20480 in the periodicity of Positioning SRS Resource.
  The TRP Tx/Rx/RxTx Timing Error Margin IE is mandatory when the associated TRP Tx/Rx/RxTx TEG ID IE is included.
  Add the SRS Positioning INACTIVE Query Indication IE into the POSITIONING INFORMATION REQUEST message to enable CU to retrieve SRS configuration and SRS-PosRRC-InactiveConfig IE (for INACTIVE) from DU
  Various correction on stage2 and stage3 specs.

## Slide 26: TEI Corrections
Progress in the last quarter
R17 SONMDT corrections:
  Allow the SN to add new cell entries with the same PSCell ID when the PSCell dewelling the time exceeds the maximum value.
  In case of CHO, the target gNB updates the UE stay time in the source Pcell and source Pscell when the target gNB receives RRC Reconfiguration Complete message from the UE.
  For SHR, discuss C-RNTI and Mobility information when the forwarding mechanism is decided.
  Correction on Resource Status Reporting procedure to avoid inter-operability issue over Xn and F1
  Various corrections on stage3 specs.

## Slide 27: RAN3 f2f Celebration Activities
Notes: w

## Slide 28: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and the post-meeting email discussion!
  Good support to the celebration activities of our first RAN3 f2f meeting after almost three years of e-meetings!
Young Ik Jo (RAN WG3 Secretary)
  For his anytime anywhere support and impressive work in the last two years!
  And welcome Seonggu to join RAN3!
Anna, Prasad, Yazid, Fenghan, Aijuan, Yanru
  For their excellent and hard work on moderating some tough email discussions and good support!
All Rapporteurs and moderators, especially Henrik, Alex
  For their efforts to R18 WIs/SIs and R17 maintenance!
  Work out the rules on RRC container reference
All RAN3 delegates
  For their positive, constructive and cooperative spirit and hard work!