## Slide 1
Discussion on work split between RAN3 and CT4 for single N2/N3 for both 3GPP Access and non-3GPP Access
- Nokia, Nokia Shanghai Bell, China Telecom, KT Corp., Intel
3GPP TSG RAN3#97
Berlin, Germany; 21st – 25th August 2017

## Slide 2: Introduction
RAN3 discussed the SA2 requirement (1) to use common N2 and N3 for both 3GPP access and non-3GPP access. RAN3 agreed following principles for NGAP:
  P1 Interface is designed targeting gNB as the RAN endpoint
  P2 Other possible nodes are assumed to support “NG terminating functionality”
  P3 AMF is assumed to be access aware via e.g. TAI
  P4 Messages may include access-specific optional IEs as needed (whether these are simply added in a flat manner, or whether optional access-specific IE groups are defined is FFS).
It is unclear about the work split between RAN3 and CT4.
This contribution analyzes the work split between RAN3 and CT4, and proposes a way forward
1. RP-170035, LS on N2 and N3 reference points for 5G system, SA2

## Slide 3: RAN3 work
As discussed in (2), RAN3 continue the NGAP specification development, i.e. business as usual with focus on 3GPP Access.
  E.g. in case the Default Paging DRX IE and RRC Establishment Cause IE are still required in NGAP, these two IEs shall be defined as conditionally present, i.e. only for 3GA.
Based on future CT4 inputs, RAN3 may take action based on CT4’s request for the extension(s) for N3GA
  Extend the common message/IE with a container for N3GA IEs. The container is defined as OCTENT STRING « encoded according to TS 29.xxx» (i.e. like existing S1AP IEs whose encoding is defined elsewhere)
    For example,
2. R3-171923, Single NGAP for both 3GPP access and non-3GPP access, Nokia, Alcatel-Lucent Shanghai Bell, AT&T, KT Corp., CMCC, China Telecom, Orange

## Slide 4: CT4 work (example only, to be discussed by CT4)
CT4 has the expertise to support the N3GA specific parts of NGAP
CT4 specifies how NGAP is used for N3GA in a new TS 29.xxx
  identifies the list of stage 3 procedures applicable to N3GA
  references 38.413 for common behaviour and messages (no duplication of spec)
  specifies N3GA specific behaviour in these procedures, if any
  specifies N3GA specific IEs in NGAP messages, if any
  specifies ASN.1 of N3GA specific extensions, if any
  In case CT4 needs to add N3GA specific IEs in a common message/IE, CT4 sends an LS to RAN3 to ask RAN3 to
  Extend the common message/IE with a container for N3GA IEs. The container is defined as OCTENT STRING « encoded according to TS 29.xxx» (i.e. like existing S1AP IEs whose encoding is defined elsewhere)
  no LS needed for common message/IE that already has an extension container

## Slide 5: Example – assuming CT4 needs to add a N3GA IE in the common message INITIAL UE MESSAGE.
  CT4 sends an LS to RAN3 asking to add a N3GA IE in INITIAL UE MESSAGE
  RAN3 specifies the following changes to TS 38.413
  CT4 specifies the following changes to TS 29.xxx

## Slide 6: N3 definition for N3GA – Proposal of work split between RAN3 & CT4
  5G extensions required for 3GA and/or N3GA defined in individual GTP-U Extension Headers or in a (R)AN Container defined as a new single GTP-U Extension Header
    see subclause 5.2.1.1 of TR 29.891
    the contents of the (R)AN Container would be specified by RAN3
    a single approach shall be selected, in coordination with RAN3
  RAN3 specifies the NG Data Transport Stage 3 in TS 38.414
  CT4 specifies the GTP-U protocol/procedures in TS 29.281
GTP-U Extensions/(R)AN Container:
  5G extensions may be common to 3GA & N3GA or access specific
  N3GA specific extensions, if any, can be defined in a different container
  RAN3 specifies the (R)AN Container, with the common and 3GA specific extensions
  CT4 identifies the extensions from the (R)AN Container applicable to N3GA
  CT4 defines N3GA specific extensions, if any
  the (R)AN Container in TS 38.415, if agreed by RAN3, includes an « extension field for N3GA » whose content is defined by CT4. (otherwise N3GA specific extensions could be specified in a separate GTP-U extension header)

## Slide 7: Conclusion
Propose RAN3 agree the work split, i.e. RAN3 part, and send a LS to CT4 regarding the work split.