## Slide 1: 3GPP TSG-RAN WG4 Meeting #100-e R4-2115641 Electronic Meeting, 16th – 27th, 2021
CATT
WF on NTN BS RF requirements (BS type 1-H)

## Slide 2: Background
NTN BS RF requirement were discussed during RAN4#100e meeting. The following contributions were reviewed.
[1] R4-2112010, Tx requirement for NTN gNB, CATT
[2] R4-2113746, NTN - Satellite Node - Tx requirements, Ericsson
[3] R4-2113932, Discussion on Tx requirements of satellite gNB, ZTE
[4] R4-2112011, Rx requirement for NTN gNB, CATT
[5] R4-2113747, NTN - Satellite Node - Rx requirements, Ericsson
[6] R4-2113933, Discussion on Rx requirements of satellite gNB, ZTE
[7] R4-2112009, Discussion on NTN gNB type/class, CATT

## Slide 3: General
  Reference point for BS type 1-H
  After 2nd round discussion, 5 companies are ok with Option 2 and 1 companies prefer FFS.
  Option 1:
  Option 2:
  Use option 2 as the starting point and further elaborate the details in the box.

## Slide 4: Tx RF requirements
Base station output power
Take the following as the starting point and further check whether co-channel co-existence study between GEO/LEO at different altitude is needed.
Radiated transmit power
Based on manufacturer declaration for each beam.
RE power dynamic range
The current RE power dynamic range should be transposed for Satellite BS if needed.
Total power dynamic range
The current total power dynamic range should be transposed depending on further discussion on SU.
Transmit ON/OFF power
This requirement is not needed for satellite BS due to FDD operation.
Frequency error
Use current 38.104 WA BS requirements 0.05ppm as the starting point and further check the impact of satellite mobility.
Modulation quality (EVM)
use current 38.104 requirements as the starting point and further check whether additional EVM is needed.
FFS on applicable modulation for satellite.
Satellite BS class | Prated,c,AC
Satellite BS class A | (Note)
Satellite BS class B | ≤ TBD dBm
Satellite BS class C | ≤ TBD dBm
NOTE: There is no upper limit for the Prated,c,AC rated output power of the Satellite BS class A. | 

## Slide 5: Tx RF requirements
Time alignment error
Further discuss whether MIMO and CA feature are in the scope of Rel-17 NTN.
Occupied BW
The current 38.104 requirement can be reused.
Operating band unwanted emission
This requirement relies on ACLR and spurious emission. It should be deferred to later stage.
Transmitter spurious emissions
Use 38.104 requirement as starting point and further check compliance to ERC 74-01 for Europe.
Protection of the BS receiver of own or different BS
This requirement is needed. FFS on the exact value.
Co-location with other BS
FFS
Transmitter intermodulation
FFS

## Slide 6: Rx RF requirements
Measurement for Rx requirement
For Rx requirements, the TAB connector is located in the satellite payload, while the throughput measurement is done in the “non-NTN infrastructure gNB”. As shown in the figure below for reference sensitivity requirement.
FRC
The FRCs specified in TS 38.104 shall be re-used to specify the satellite node Rx requirements. Further revisit is not precluded if the SU is different.
Reference sensitivity
Further discuss this issue, including SNR, NF, implementation etc…

## Slide 7: Rx RF requirements
OTA sensitivity
Use the requirement in 38.104 as the starting point and further check during performance part of the WI.
Dynamic range
For further study.
ACS、in-band blocking
Wait for the co-existence simulation results
Out-of-band blocking
For further study.
Co-location requirement
FFS
Receiver spurious emission
This requirement should be transposed for satellite BS.
Receiver intermodulation
FFS
In-channel selectivity
The requirement frame work can be reused. FFS on details.