## Slide 1
33GPP TSG-RAN WG4 Meeting # 111 R4-2408387
Fukuoka, Japan, May. 20th – 24th, 2024
Source: ZTE Corporation, Sanechips
Agenda Item: 13
Motivation on R19 basket WID on NR intra-band contiguous CA with UL MIMO

## Slide 2: Backgroud (1)
In TS38.101-1 v18.5.0, there are two PC2/3 NR intra-band CA configuration with UL MIMO defined, i.e. CA_n41C, CA_n78C
In the R19 WID NR_ENDC_RF_Ph4, there are four NR intra-band CA configuration with UL MIMO selected as example band combination, i.e. CA_n41C, CA_n78C, CA_n77C and CA_n79C
  Also there was a note in the objectives, saying: NOTE: leave the other band combination specific requirements to the corresponding Rel-19 basket WIs
NRCA Configuration | Class 1 (dBm) | Tolerance (dB) | Class 2 (dBm) | Tolerance (dB) | Class 3 (dBm) | Tolerance (dB) | Class 4 (dBm) | Tolerance (dB)
CA_n41C |  |  | 26 | +2/-31 | 23 | +2/-31 |  | 
CA_n78C |  |  | 26 | +2/-3 | 23 | +2/-3 |  | 
NOTE 1: If all transmitted resource blocksover all component carriers are confined within FUL_lowand FUL_low + 4 MHz or/andFUL_high– 4 MHz and FUL_high, the maximum output power requirement is relaxed by reducing the lower tolerance limit by 1.5 dBNOTE 2: PPowerClassis the maximum UE power specified without taking into account the tolerance |  |  |  |  |  |  |  | 

## Slide 3: Backgroud(2)
In RAN4 #110 meeting, some missing lower order power class(PC2 and PC3) of same PC1.5 band combination were observed (also shown in the previous slide). How to treat the new proposed BC configurations for intra-band CA which are not included in the NR_ENDC_RF_Ph4 WI objectives were included in the WF[2], which are shown below:

## Slide 4: Motivation
There are a lot of NR FR1 bands supporting intra-band contiguous CA operation, meanwhile UL MIMO feature can also be supported in the same band.
There are two bands specified NR CA configurations with UL MIMO in the existing TS38.101-1 specification, the general RF requirements have already been defined.
In the R19 WID NR_ENDC_RF_Ph4, there are several PC1.5 NR CA configurations with UL MIMO included, however the corresponding lower power class (i.e. PC2/PC3) configurations are missing in some of them (i.e. CA_n77C and CA_n79C).
  The absence of a lower power class configuration would cause problems in duty cycle based SAR solution to high power class configuration.
Moreover, considering the demands from operators, and more NR intra-band UL contiguous CA with UL MIMO will be supported, using Basket WID approach should be an efficient and routine way.
Therefore, it is proposed to create a Rel-19 basket WID to include new NR intra-band UL contiguous CA with UL MIMO.
  PC2 and PC3 intra-band UL contiguous CA with UL MIMO can be included firstly, PC1.5 intra-band UL contiguous CA with UL MIMO can be considered after the general requirements are completed in R19 WID NR_ENDC_RF_Ph4.

## Slide 5: Proposals
Proposal: It is proposed to create a Rel-19 basket WID to include new NR intra-band UL contiguous CA with UL MIMO.
  PC2 and PC3 intra-band UL contiguous CA with UL MIMO can be included firstly, PC1.5 intra-band UL contiguous CA with UL MIMO can be considered after the general requirements are completed in R19 WID NR_ENDC_RF_Ph4.

## Slide 6: Rerference
  1. RP-240828, New WID: UE RF enhancements for NR FR1/FR2 and EN-DC, Phase 4, RAN4 chair (Huawei)
  2. R4-2406583, WF on HPUE UE for UL CA and EN-DC, Samsung

## Slide 7: Thank you