## Slide 1: Views on Fragmented Carriers in Rel-19
MediaTek Inc.
3GPP TSG-RAN WG4 Meeting # 111 R4-2408619
Fukuoka City, Fukuoka, Japan, 20th - 24th May, 2024 Agenda Item 13

## Slide 2: Background
A WF was agreed in RAN-P#103 and some operators band combo information were provided
Example bands in CA:
[1] RP-233374, “Fragmented carriers in the DL”, TELUS, Bell Mobility, Telstra, Nokia, Nokia Shanghai Bell, AT&T, US Cellular
[2] R4-2402309: “Study on effective utilization of fragmented FR1 carriers in the DL”, TELUS, Bell Mobility, Telstra, Nokia, Nokia Shanghai Bell, AT&T, US Cellular

## Slide 3
Scope (Agreed WF)
Objectives:
  Identify methods for reducing number of UE Rx chains (e.g. 1 or 2) needed for single DL band of ≤ 100 MHz (frequency span) containing two non-contiguous CCs within a CA combination for the inter-operator co-located scenario, considering:
    Which RF requirements could be adjusted for the inter-operator co-located scenario, e.g. Existing UE RF requirements such as ACS
    The ability to semi-statically switch hardware resources (i.e., Rx chains) between bands
    6 dB power imbalance between the two non-contiguous CCs
    Impacts on DL performance
    Means for a UE to inform the network of new CA configuration it can support with adjusted RF requirements
RAN4 led item with minimal RAN2 impact and no RAN1 impact is foreseen
Timescale:
  Start Q3 2024
  Target completion Q2 2025
Note: When the study is complete, consider normative work to define core requirements using the identified solution
P
S
P
S
T
R
FDD band
FDD band consideration:
1. Existing NCCA requirements can be starting point
2. Based on current (ΔRIBNC), study further relaxation due to sharing receiving path that UE can support the new feature
3. Need example combo configuration

## Slide 4: Receiver Architecture Reference
Type 1 UE: Shared receiver design
CC0
CC1
CC0
CC1
Ant X
Ant0
iLNA
BQ
eLNA
BQ
RX1
RX2
RX1
RX2
Capable suport X-layer MIMO / X-Rx diversity
Ant0
iLNA
BQ
eLNA
RX1
DAC
Alternative shared receiver design
CC0
CC1
CC0
CC1
Carriers are handled/separated in DBB (Digital BaseBand)

## Slide 5
Separate Rx receiver chain reference design blockdiagram
Type 2 UE: Separate receiver path
iLNA
BQ
eLNA
Ant X
Ant0
CC0
CC1
Capable support X/2-layer MIMO, X/2-Rx diversity

## Slide 6
Operators Wish List
CA_n7(2A)-n25(2A)-n66(2A)-n77(3A)
CA_n25(2A), n71(2A), n66(2A) and n41(2A)
CA_n2(2A)-n66(2A)
CA_n7A/B-n26(2A)-n78(2A), a real deployed network
Complicated CA in Rel-18 (at least two NCCA bands):
CA_n1A-n3A-n7B-n26(2A)-n78(2A)
CA_n25(2A)-n41(2A)-n66A-n71A
CA_n25A-n41(2A)-n66A-n77(2A)
CA_n7(2A)-n25(2A)-n66(2A)-n78(2A)
We see operator wish on higher order configurations. We also see there are some high-order non-contiguous spectrum configurations in existing specs that are not easy for UE implementation. To resolve implementation difficuly on high-order configurations, we propose to begin with studying fundmental configurations.
Proposal 1: We propose to start with the study of single DL band with the criterias in the agreed WF
Notes: Not possible to resolve all problems. Proposal: we can start from simple case as starting point (ex: n7(2A)

## Slide 7: Self-Band UL Impact
In the existing specs for downlink non-contiguous carrier aggregation (DL NCCA), ΔRIBNC were specified on SCC for FDD bands due to the impact of self-band uplink carrier. It’s difficult to preclude this factor so that it may still need to be considered in this study work.
Observation 1: UL configuration may have impact on SCC DL performance that would need to be considered

## Slide 8: Possible Aspects
Receiver sharing path:
  Inter-operator, collocated: Focus on RAN4 UE RF requirements study first, keep no RAN1 spec impact.
    FDD: Allow degradation (ΔRIBNC) and study further relaxation due to sharing receiving path that UE can support the new feature
    TDD: Study on DL carrier degradation (ΔRIBNC,TDD) due to sharing receiving path that UE can support the new feature with higher-order configurations
    Observation 2: Different duplex mode can be studied separately
Signaling impact:
  UE hardware configuration may be changed if new signaling is indicated
  Suggest scope may need to be limited to applicable complexity on signaling change
  There is inter-band CA with DL overlapping frequency in existing RAN4 requirements. If the solution of fragment spectrum also intends to cover such operation, UE implementation may be difficult on the control flow
  Proposal 2: Focus on inter-band CA with non-overlapping DL frequency rang under NR stand-alone

## Slide 9: Thank you!