## Slide 1: Tx switching for 3Tx UEs
MediaTek Inc., China Telecom, China Unicom, OPPO, Softbank, T-Mobile USA, Verizon
3GPP TSG-RAN WG4 Meeting # 113 R4-2417905
Orlando, US, 18th – 22nd November, 2024 Agenda Item 10

## Slide 2: Introduction
Rel-18: first step toward 3Tx via:
  WI 4Rx_low_NR_band_handheld_3Tx_NR_CA_ENDC (non-spectrum)
  WI R18_3Tx_NR_CA_ENDC. (spectrum)
  3Tx chains on top of PC2 and PC1.5  config flexibility for UL-MIMO with UL CA  BetterUL Tput
In Rel-19,
  In NR_ENDC_RF_Ph4, one objective is to specify HPUE with CA for 3Tx UE.
  RAN#104: per the approved spectrum WIDs in RP-240894, the 3Tx requirements will be distributed into misc. baskets, incl.
  DC_R19_xBLTE_yBNR/NR_CADC_SUL_R19 for PC3
  HPUE_DC_LTE_NR_R19/HPUE_NR_CADC_SUL_R19 for HPUE.
In Rel-19, the addition of FDD 2Tx + TDD 1Tx for 3Tx UE requirements is a key difference vs Rel-18

## Slide 3: Motivation
“FDD 1Tx + TDD 2Tx” and “FDD 2Tx + TDD 1Tx” UL configurations are both specified today – but dynamic switch between these configurations is not allowed in the current UL Tx switching framework
   Negative impact on the achievable UL performance
With Dynamic Tx switching, network can fully utilize the UE Tx capability to maximise the UL throughput, e.g.
  TDD 2Tx + FDD 1Tx during the TDD UL slots when the UE experiences good channel conditions
  TDD 1Tx + FDD 2TX when TDD channel conditions is worse, or during the TDD DL slots
U
U
U
U
FDD
D
D
D
S
TDD
U
U
U
U
D
D
D
D
U
U
U
U
FDD
D
D
D
S
TDD
CC#1
U
U
U
U
D
D
D
D
D
D
D
S
TDD
CC#2
U
U
U
U
2Tx
1Tx
switch period
Worse TDD conditions or DL slots
Good TDD conditions

## Slide 4: Expected specification impacts
  Main discussions on how to re-use legacy requirements
  RAN1: TS 38.214: Text updates to add the new cases. (e.g., Section 6.1.6.2)
  RAN2: TS 38.331: New RRC parameter to configure the UE with the feature
    TS 38.306: Corresponding UE capabilities
  RAN4: TS 38.101-1: New section or new applicability rule for ON-OFF mask requirements (e.g., Section 6.3A.3.3).
    TS 38.133: New section or new applicability rule for interruption requirements (e.g., Section 8.2.2.2.10)
          Draft CR for 38.214
          Draft CR for
          38.101-1
          Draft CR for
          38.133

## Slide 5: Proposal & Objectives
  Specify dynamic UL Tx switching between FDD 1Tx + TDD 2Tx and FDD 2Tx + TDD 1Tx as a Rel-19 feature, with the following objectives:
    Extend existing physical layer UL Tx switching framework to support the new switching cases [RAN1]
    Specify RF and RRM requirements to enable the new switching cases [RAN4]
    Specify configuration and UE capability RRC signalling for the feature [RAN2]

## Slide 6: Thank you!