## Slide 1: TSG-RAN Working Group 4 (Radio) meeting #58 R4-111548 Taipei, Taiwan, 21 – 25 February, 2011 Source: Vodafone Title: LTE MIMO OTA Measurement Campaign – Final eNodeB emulator Parameter settings Agenda item: 7.3 Document for: Approval

## Slide 2
Table B.2.4.1: eNode B emulator setting parameters
Parameters |  | Signal Level | 
 |  | Middle | High
Connection mode of UE |  | Attached | 
DL MIMO mode |  | 2 x 2 open loop spatial multiplexing | 
Duplex mode |  | FDD | 
Operating band (UL channel, DL channel) |  | band 7 (21100, 3100) band 20 (24300, 6300) | 
Schedule type |  | Reference Measurement Channel (RMC) | 
Reference Channel |  | R.11(Note 1) | R.X (Note 2)
Bandwidth DL | MHz | 10 | 
Number of RBs DL |  | 50 | 
Start RB DL |  | 0 | 
Modulation DL |  | 16QAM | 64 QAM
TBS Idx DL (MCS Idx DL) |  | Defined by RMC 14 (15) | Defined by RMC [24] ([26])
Bandwidth UL | MHz | 10 | 
Number of RBs UL |  | 50 | 
Start RB UL |  | 0 | 
Modulation UL |  | QPSK | 16QAM
TBS Idx UL (MCS Idx UL) |  | Defined by RMC 6 (6) | Defined by RMC 19 (20)
Transmit power control | dBm | -10, open loop (Note 3) | 
PBCH_RA = rA | dB | -3 | 
PBCH_RB = rB | dB | -3 | 
Number of HARQ transmissions |  | 1 | 
AWGN |  | OFF | 
Number of subframes for FOM measurement |  | 20,000 (for fading) | 
DL power level (RS EPRE) | dBm / 15 kHz | Set at eNodeB simulator with correction from calibration | 

## Slide 3
Parameters are aligned for:
  CMW 500
  Anritsu MTC8820C
  AT4 S3110B
Note 1: This RMC is defined in 3GPP TS 36.521-1, subclause 8.2.1.3.1
Note 2: This RMC has not yet given name in RAN5
Note 3: Uplink power control is switched off
Notes