## Slide 1: Discussion and background on AAS conducted requirements for Rel-12
Document for: Discussion
Huawei
3GPP TSG-RAN WG4 meeting #70
Prague, Czech Republic, EU, 10th – 14th February 2014
This is the accompanying background document for the way forward on conducted requirements, the contents are background provided by WF proponent and are NOT for approval

## Slide 2: Background
For conducted requirements at transceiver array boundary, it is proposed in R4-140256 and R4-140257 to limited the number of transceivers <=8 for Rel-12 AAS specification.
It is also proposed in the above Tdocs to apply the existing requirements in TSxx.104 series expressed per antenna connector to each AAS transceiver.
  This implies that the OOB and spurious emission is not “scaled” for number of transceivers <=8 following 3GPP approach
There were offline discussions on the regional requirements on OOB and spurious emission.
OOB: operation band unwanted emission

## Slide 3: Purpose of this slide
Purpose 1: To clarify how the AAS applications, such as cell partitioning and UE-specific beam forming, to be supported by AAS with number transceivers <=8.
Purpose 2: To propose how to handle the different requirements in different regulation (pending further confirmation) and standardization bodies on OOB and spurious emission requirements across multiple antenna connectors.

## Slide 4: AAS structures: H4xV1, cross polarization
Antenna 1 and 2
Antenna 3 and 4
Antenna 5 and 6
Antenna 7 and 8

## Slide 5: AAS structures: H4xV1, cross polarization
Conventional 8 antenna
Horizontal cell partitioning is supported.
The largest number of radiation elements, the worst case of emission level of spurious emission.
The 3GPP requirements for spurious emission is per antenna connector.

## Slide 6: AAS structures: H2xV2, cross polarization
cell partitioning and
UE specific beam-forming
can be supported
Number of radiation
elements is half of H4xV1
Total spurious emission
level is reduced by half

## Slide 7: AAS structures: H1xV4, cross polarization
Cell partitioning and
UE specific beam-forming
can be supported
Number of radiation
elements is 1/4 of H4xV1
Total spurious emission
level is reduced by 1/4 of H4xV1

## Slide 8: For # of TRX(s) <=8
UE specific beam-forming and cell partitioning can be supported.
The worst case of spurious emission level is H4xV1 (dual polarization), which is the conventional 8 antenna installation, where 3GPP spurious emission level is applied at each antenna connector.

## Slide 9: Requirements in different regions and in 3GPP
The “3GPP approach” for OOB and spurious emission is apply the existing requirements per antenna connector.
The “3GPP approach” might have been deployed in some regions as regulations.
Some other regions may require “scaling” of OOB and spurious emission level across multiple antenna connectors (to be confirmed).
  FCC
  Others

## Slide 10: Suggested AAS specification solutions
In view of different requirements in 3GPP and some regions on OOB and spurious emission, it is suggested to define different “categories” of requirements on OOB and spurious emissions across multiple antenna connectors.
This is very similar to the existing Category A and Category B OOB requirements to address requirements in different region.
“3GPP approach” can be the generic approach.

## Slide 11: On OOB emission (not limited to number of TRX<=8)
Basically, there are two requirements for adjacent channel coexistence: SEM for OOB and ACLR.
It should be noted that the coexistence performance is primarily governed by the per antenna connector ACLR performance.
It may not be necessary to tighter the SEM by scaling across the multiple antenna connectors.

## Slide 12: On other requirements other than OOB and spurious emissions
For other Tx and Rx requirements other OOB and spurious emissions, the existing requirements expressed at each antenna connector apply to each transceiver at the transceiver array boundary.

## Slide 13: Summary
To limit the number of TRX(s) <=8 for Rel-12 AAS specification. Others are for future.
  In 3GPP specification, to apply existing per antenna connector conducted requirements for each transceiver.
  The worst case emission level is what currently be specified and deployed 8x1 antenna. The other configurations, such as 4x2, 2X4, and 1x8 have less radiation elements and therefore less emission level.
Different requirement “category” may be specified for regional requirement for multiple antenna connector for OOB and spurious emission.