## Slide 1
3GPP TSG-RAN WG4 Meeting#71 R4-142847
Seoul, South Korea, 18 - 23 May, 2014
Agenda item: 7.31.1
Source: KDDI
Document for: Approval
Title: Way Forward on UE REFSENS for CA_1A-28A

## Slide 2: Background
CA_1A-28A is classified as Class A2.
Working assumption on UE architecture has been extensively discussed in several meetings.

## Slide 3: Point to be discussed
Is Harmonic Trap Filter needed for CA_B1-B28?

## Slide 4: Without trap filter
Harmonic trap filter plays a quite important role when one suffers from harmonic interference but also provides 0.5dB loss in always both for Tx and Rx side.

## Slide 5: With trap filter
Situations in certain Region have been unclear.
Issue caused by 3rd Harmonic can be avoided in operational perspective (not to use B28 UL in CA mode).

## Slide 6: Proposed Way Forward
Following way forward should be approved.
  WF: Standardize CA_B1-B28 in assumption without Harmonic Trap Filter.