## Slide 1: WF on interruption handling for inter freq/RAT measurement in Rel.12
NTT DOCOMO
R4-143902
3GPP RAN4 #71 meeting
Seoul, Korea

## Slide 2: Way forward
In order to utilize inter frequency/RAT measurements on unused RF chain, visible interruption should be considered to be introduced in Rel. 12.
  Visible interruption should be synchronized between CCs
  ML, VIL, VIRP in the following figure is to be specified in RAN4
    Supported VIL is reported by UE for each band in a CA band combination
    UE supporting the visible interruption shall indicate NeedForGaps as true.
    VIRP and ML have an default value which will be decided by RAN4
It is not precluded to do further analysis on alternative solutions
VIL
ML
VIL
VIRP
ML: Measurement Length
VIL: Visible interruption length
VIRP: Visible interruption Repetition Period

## Slide 3: Way forward
RAN4 can take the following numbers as baseline for its further consideration
  ML: 4 or 5 or some value reported from UE
  VIL: 1 or some value reported from UE
  VIRP: 40 or 80 or some other values