## Slide 1: Way forward on 2UL inter-band CA MSD test configurations
Agenda Item: 7.35
Document for: Approval
Source: MediaTek Inc., TeliaSonera
3GPP TSG-RAN WG4 Meeting #71 R4-144031
Seoul, Korea, May 19th -23rd, 2014

## Slide 2: Principles for MSD Test
Choose a specific carrier frequency allocation such that IMD is center-aligned with victim DL carrier to attest the worst-case self-desensitization condition.
Choose 5-MHz bandwidth with full RB for all carriers (if supported in a CA combination) to essentially comply with the Rel-8 UL configurations for REFSENS tests and approach the worst-case self-desensitization condition.
If 5-MHz bandwidth is not supported in certain CA combinations, then choose 10 MHz with full RB or the RB number which complies with Rel-8 UL configurations for REFSENS tests.

## Slide 3: Principles for MSD Test - Continued
For B2_B4, IMD3 can overlap with DL carrier only when B2 carrier bandwidth is at 20 MHz. 50 RB is configured with RBstart = 0 for B2 UL to avoid spectral leakage impact.
A correction factor (CF) is calculated to address the power difference between the total IMD power and the power within DL carrier modulation bandwidth.

## Slide 4: Way Forward
To agree on the test configurations as proposed in R4-144031 Table 3-1 which is derived based on the aforementioned principles.
Companies to base on R4-144031 Table 3-1 to calculate IMD level with CF and derive MSD as test requirement.
Develop the test configurations into core specifications.