## Slide 1
3GPP TSG-RAN WG4 Meeting #71 R4-144047
Seoul, South Korea, 19 - 23 Mai 2014
Source: TeliaSonera
Title: WF on spurious emission levels/ranges and AMPR simulations
Agenda item: 4.2.1.1
Document for: Approval
___________________________________________________________________________
The group decided to consider the following four cases for further discussion on B42/B43 UE-coexistence:
1) -15.5dBm/5MHz at 5MHz offset from the aggressor over a 25 MHz region
-40dBm/MHz at 30 MHz offset from the aggressor to the end of the band
2) -15.5dBm/5MHz at 5MHz offset from the aggressor over a 20 MHz region
-40dBm/MHz at 25 MHz offset from the aggressor to the end of the band
3) -23dBm/5MHz at 5MHz offset from the aggressor over a 25 MHz region
-40dBm/MHz at 30 MHz offset from the aggressor to the end of the band
4) -23dBm/5MHz at 5MHz offset from the aggressor over a 20 MHz region
-40dBm/MHz at 25 MHz offset from the aggressor to the end of the band

## Slide 2
20MHz E-UTRA
-15.5dBm/5MHz
OR
-23dBm/5MHz
-40dBm/MHz
5MHz
offset
25 OR 30MHz
B42 B43
Companies are invited to perform simulation of needed AMPR for those cases. The decision on which case(s) shall be used for NS/AMPR signalling could be based on balancing DL interference to victim UEs and UL AMPR levels needed for the aggressor.
AMPR simulations for single carrier and CA
No Tx RF filter is considered for that simulations
The offset for which no AMPR is needed should be computed
From 0 to 5 MHz no spectrum emission will be defined in the NS_xx table