## Slide 1: MU discussion for harmonization campaign
Source： NTT DOCOMO
Agenda Item: 7.3.3
Document for: Discussion
3GPP TSG-RAN WG4 #76 R4-154433
Beijing, China, 24-28st , August, 2015

## Slide 2: Introduction
Applying hybrid MU is agreed in RAN4 #75 [1].
It is not concluded that some additional factor for MU bound is need or not. (How do we handle proposal 3 as shown below ?)
  Proposal 3: The group agrees to apply the hybrid MU bound defined in R4-153766 directly to the harmonization analysis without additional factors
It is proposed that best fit approach to selecting the harmonization offset in con. call #4 with regard to the fixed offset among methodologies.
This contribution is to promote the MIMO OTA discussion with regard to harmonization campaign.
  Potential solution of MU bound and how to define fixed offset

## Slide 3
ADTF radiated testing 1
ADTF radiated testing 2
b1
Potential expanded MU bound
Composite MU bound (+/-(a+b))
defined in R4-153766 [1]
b2
Time period
ADTF testing 1
DUT 1
DUT 2
DUT 3
DUT 4
ADTF testing 2
Harmonization Campaign
When testing interval is very large, ADTF radiated testing results may fluctuate larger than original
composite MU bound (agreed in [1]) as shown below. Because the non-linear equipment
(e.g. channel emulator or PA) change their characteristics by temperature or other conditions.
Considering that harmonize campaign is done in long term, this effect should be taken into account.
Concerned situation for MU bound
If CATR measure ADTF testing on different day (e.g. every two or three weeks) in each methodology, it is no concern to apply hybrid MU bound directly without any additional factor. But, if not,
our preference is to do ADTF radiated testing several times (at least twice with a few weeks period)
If it could not, some additional MU should be included (e.g. +/- ((a+b) +0.5) dB).
RSEPER
RSEPER

## Slide 4
Fixed offset
ADTF radiated testing in meth. A
ADTF radiated testing in meth. B
b1
Present fixed offset
Composite MU bound (+/-(a+b))
defined in R4-153766 [1]
b2
Methodology A
Methodology B
Range of potential fixed offset
Fixed offset value among methodologies is derived from ADTF results in our understanding.
Considerable way of best-fit approach is as follows.
DOCOMO agrees to apply a best-fit approach to selecting the harmonization offset for this
harmonization campaign proposed in Con. Call #4. This slide shows the clarification for best
fit approach.
Δ1
Δ2
RSEPER
RSEPER
Fluctuation of ADTF results should be considered when fixed offset is defined.
Fixed offset is defined to harmonize measurement results in the range of Δ1 to Δ2.

## Slide 5
Fixed offset (applying MU bound)
MU bound
Methodology A
Methodology B
Δ1
Δ2
Fixed offset is defined to harmonize measurement results in the range of Δ1 to Δ2.
RSEPER
RSEPER
There may be some other ideas of best fit approach. This is our understanding based on
the Motorola proposal in con. cal #4 [2].
If it is not correct, we would like to discuss and understand further.
Below image shows an example of MU bound after applying fixed offset.

## Slide 6: Conclusion
Mu bound : It seems to be need to consider in other aspect as shown in this contribution (it is may not be additional factor.).
Fixed offset : Fluctuation of ADTF testing should be considered if fixed offset derives from ADTF results.
Our preference is to define appropriate MU bound and fixed offset (not too tight and not too relaxed).

## Slide 7: References
[1] R4-153766, “A hybrid approach determining the measurement uncertainty bounds for the harmonization measurement campaign.”, Motorola Mobility, Spirent Communications, Intel Corporation, Rohde & Schwarz, CATR, MVG, Anite, SGS Wireless, RAN4#75
[2] R4-15xxxx, “The implementation of the hybrid approach determining the measurement uncertainty bounds for the harmonization measurement campaign. ”, Motorola Mobility, RAN4#76