## Slide 1: How to handle harmonic mixing issue in RAN4
KDDI Corporation
3GPP TSG-RAN WG4 #76-bis
Sophia Antipolice, France, 12 – 16 October, 2015
Agenda Item: 5.1.2
Document for: Approval
R4-155819

## Slide 2: Background
How to handle harmonic mixing issue has been discussed almost for one year but there is no agreement in RAN4.
In this contribution, we would like to make a proposal for closing this issue.

## Slide 3: Analysis
During our internal studies, it was clarified that de-sense due to harmonic mixing would be observed only in specific case.
If L/O is square wave based, harmonic across mixing process would be larger than when L/O is sine wave based.
Policy on choosing which L/O is out of scope of 3GPP specification. Thus, we make proposals in the next slide.

## Slide 4: Proposal
Harmonic mixing issue should be understood as implementation issue. Therefore, RAN4 should not specify any MSD requirements due to harmonic mixing into TS.
TR can include MSD due to this issue as informative annex.
In order to pass RAN5 test requirement(s), TS36.101 should imply that de-sensitization might occur in certain CA combinations and no requirement applies on this issue.