## Slide 1: Way forward on Bands for 4AP receiver
Ericsson
3GPP TSG-RAN WG4 Meeting #76bis R4-156285
Sophia Anti-Polis, France, 12 – 16 October, 2015

## Slide 2: Discussions
Receiver requirements are band agnostic in general except the REFSENS requirements.
  We should focus more on the actual requirements instead of the potential bands for the feature
In order to complete the receiver requirment work in a timely manner, a handful of representative bands can be considered in step-1
The down selection of a few bands ensure the completion of receiver requirements in time
  Other bands are not excluded from considerations

## Slide 3: Proposals
Treat following bands in step-1 to complete the RF specification work
  FDD bands: 1, 3, 4, 7, 20 and 28
  TDD bands: Band 41 and band 42
Any other operating band(s) can be added as 4Rx band once step-1 is completed under the current WI
  Only REFSENS discussions are needed for new bands
If the requirements related to at least one low band, at least one high band and at least one TDD band are completed, the WI can be concluded.
Beyond the current WI timeframe, how a new band can be added as 4RX capable is FFS