## Slide 1: Way Forward on Simulation Assumptions and Methodology for NB-IOT coexistence study
[Qualcomm, Ericsson, Nokia Networks, Huawei,…]
R4-156750
3GPP TSG-RAN WG4 #76bis
Sophia Antipolis, France, 12 -16 Oct, 2015
Agenda Item: 7.50.2.1

## Slide 2: References
GERAN TR 45.820
TR 36.942
TR 25.942
Company Contributions:
[1] RP-151621, “New Work Item: NarrowBand IOT (NB-IOT)”, Qualcomm
[2] R1-156022, “NB LTE - Inband UL coexistence evaluation”, Ericsson
[3] R4-155525, “NB-IOT Coexistence study for guard band operation”, Huawei, Hisilicon
[4] R4-155524, “NB-IOT Coexistence study for stand-alone operation”, Huawei, Hisilicon
[5] R4-156256, “Scenarios and simulation assumptions for NB-IoT co-existence study”, Ericsson
[6] R4-156321, “Simulation Assumptions NB-IoT Coexistence”, Qualcomm
[7] R4- 155949, “Discussion on co-existence study for NB-IoT”, Nokia
[8] “Chairman's Notes RAN1_82bis”

## Slide 3: Use Cases
RAN4 should consider the following use cases:
1. Stand-alone operation
  NB-IoT and the legacy system are non co-located (NB-IoT is at the cell edge of the legacy system). Network layout is as shown in figure 4.3 in 36.942
2. Guard band operation
  NB-IoT and the LTE are Co-located
3. In-band operation
  NB-IoT and the LTE are Co-located

## Slide 4: Evaluation Methodology for stand-alone
Static system simulation
Input parameter for all simulations should be ACS and ACLR of NB-IoT
  ACIR is calculated as shown in 45.820
The results should be presented as a function of ACS (when NB-IoT is victim) and as a function of ACLR (when NB-IoT is aggressor)
Metrics:
  For NB-IoT use SINR
  For GSM use SINR and outage increase
  For UMTS use capacity loss
  For LTE use SINR and throughput loss (based on SINR to throughput mapping in 36.942)

## Slide 5: Evaluation methodology for In-band and guard band operation
There is no agreement on the evaluation methodology for in-band and guard band operation
Companies are encouraged to provide simulation results based on preferred methodology

## Slide 6: Aggressor/Victim configurations for different use cases (to be completed)
Use Case | Aggressor | Victim
Stand-alone operation | NB-IOT DL | GSM/UMTS/LTE DL
Stand-alone operation | GSM/LTE/UMTS DL | NB-IOT DL
Stand-alone operation | NB-IOT UL | GSM/UMTS/LTE UL
Stand-alone operation | GSM/UMTS/LTE UL | NB-IOT UL
Guard band operation | NB-IOT DL | LTE DL
Guard band operation | LTE DL | NB-IOT DL
Guard band operation | NB-IOT UL | LTE UL
Guard band operation | LTE UL | NB-IOT UL
In band operation | NB-IOT DL | LTE DL
In band operation | LTE DL | NB-IOT DL
In band operation | NB-IOT UL | LTE UL
In band operation | LTE UL | NB-IOT UL

## Slide 7: General Simulation Assumptions
Carrier Frequency = 900MHz
Propagation model: as in TR 36.942
Inter-site distance
  1732m for coexistence with GSM
  750m for coexistence with UMTS and LTE
System loading: full buffer
System activity: 100% (optional 30%)

## Slide 8: NB-IOT Simulation Assumptions
NB-IOT system bandwidth: 200KHz
BS Tx Power:
  43dBm/200KHz for stand-alone,
UE Tx Power: -40dBm to 23dBm
Power Control
  DL: no PC
  UL: based on sub-clause 5.1.1.6 of 3GPP TR 36.942.
    Alpha: 1, full path-loss compensation
    P0 is calculated from CLx-ile.
    CLx-ile should be adapted it to path loss formula
UE antenna gain: -4dBi
Building penetration loss is taken from Annex D.1 of TR 45.820 (No additional building penetration loss for the NB-IoT as aggressor)
BS ACLR: [40,45,50,55,60] dB
BS ACS: [40, 45, 50]dB
UE ACLR: [30, 35, 40, 45, 50]dB
UE ACS: [30, 35, 40]dB

## Slide 9: GSM Simulation Assumptions
BS Tx Power: 43dBm
UE Tx Power: 5dBm to 33dBm
Power Control
  DL: no PC
  UL: CS power control based on 25.816
Frequency reuse: 4/12
ACLR for BS and UE are derived from 3GPP TS 45.005, with the assumption that ACLR for the base station includes both wideband noise emissions and IM products.
ACS for BS and UE are derived from 3GPP TS 45.005, under the condition that a guard band of 100 kHz or more between NB-IoT and GSM is assumed.

## Slide 10: UMTS Simulation Assumptions
Baseline assumptions in TR 25.942
System bandwidth: 5MHz
BS Tx Power: 43dBm
UE Tx Power: -50dBm to 21dBm
Power Control
  DL: according to 25.942
  UL: according to 25.942
BS ACLR and ACS: according to 45.820
UE ACLR and ACS: according to 45.820

## Slide 11: LTE Simulation Assumptions
Baseline assumptions in TR 36.942
System bandwidth: 10MHz
BS Tx Power: 46dBm
UE Tx Power: -40dBm to 23dBm
Power Control
  DL: no PC
  UL: according to 36.942
BS ACLR and ACS: 45dB and 45dB
UE ACLR and ACS: 30dB (for ACLR1) , and 43dB (for ACLR2) and 33dB (for ACS)