## Slide 1: Way forward on Band definition for LAA operation
Ericsson, Qualcomm, Nokia Networks, Intel, Sony Mobile, T-Mobile USA, Deutsche Telekom, Verizon Wireless, LG Electronics, MediaTek Inc., Alcatel-Lucent
3GPP TSG-RAN WG4 Meeting #76bis R4-156785
Sophia Anti-Polis, France, 12 – 16 October, 2015

## Slide 2: Way forward
1) LAA operation is defined with a single operating band with the frequency range of 5150-5925MHz.
2) Sub-bands can be introduced in the BS specification in order to reflect specific regulatory requirements or restrictions.
3) The duplex method for 5GHz unlicensed band will be TDD subject to RAN1 design of new frame structure.
  UL requirements are not defined in this version of specifications.

## Slide 3: Example implementation in 36.104
Following can be one of the ways of including subband notations in 36.104
Sub-band | Frequency range | 
[45A] | 5150 – 5250 MHz | 
[45B] | 5250 – 5350 MHz | 
[45C] | 5470 – 5725 MHz | 
[45D] | 5725 – 5925 MHz | 
Table 5.5-1A Band [45] sub-bands for LAA BS