## Slide 1: Way Forward on 4Rx CSI performance
Ericsson,
3GPP TSG-RAN WG4 Meeting #76bis R4-156862
Sophia Antipolis, France, 12th – 16th Oct 2015

## Slide 2: Agreements in 4Rx Adhoc
Tests from the CSI WF are further discussed, and if necessary email discussion on RAN4 reflector will be used to reach a list of tests to be evaluated for next meeting.

## Slide 3: Way Forward for 4Rx CQI performance
Evaluate the CQI testcases for on next page.

## Slide 4: 4Rx CQI performance
Propagation condition | Reporting | TM | Proposed antenna configuration | # of Layers | Based on current requirement | Proposed by
AWGN | PUCCH 1-0 | TM1 | 1x4 | 1 | 9.2.1.1 | Huawei
AWGN | PUCCH 1-1 | TM4 | 4x4 | 2 , 3 & 4 | 9.2.2.1 | Intel, Huawei
AWGN | PUCCH 1-1 | TM9 | 4x4 | 3 & 4 | 9.2.3.1 | Ericsson, Intel, Huawei
EPA5 | PUCCH 1-0 | TM 4 | 4x4 | max rank 4 | 9.3.2.1 | Nokia
EPA5 | PUCCH 1-1 | TM9 | 4x4 |  | 9.3.2.2: | Ericsson, Nokia
EPA5 | PUCCH 1-0 | TM1 | 1 x 4 | 1 | 9.3.5.1 | Intel
EPA5 | PUCCH 1-1 | TM9 | 2x4 /4x4 | 1 | 9.3.5.2 | Ericsson, Intel, Huawei
EVA5 | PUCCH 3-1 | TM 4 | 2x4 | max rank 2 | 9.3.1.2 | Nokia
EVA5 | PUSCH 3-2 | TM6 | 4x4 |  | 9.3.7 Test 1 | Ericsson
EVA5 | PUSCH 3-2 | TM9 | 4x4 |  | 9.3.7 Test 2 | Ericsson, Nokia
EVA5 | TBD | TM9 | 4x4 |  | Enhanced Receiver Type C | Ericsson, Nokia

## Slide 5: Way Forward for 4Rx PMI performance
Evaluate if PMI testing by using PMI feedback in the Layer 3&4 testcases is acceptable
Evaluate the PMI testcases on next page

## Slide 6: PMI
Propagation condition | TM | Proposed new antenna configuration | # of Layers | Based on current 2Rx requirement section | Proposed by
EVA5 | TM9 | 4x4 or 8x4 | 2, 3 or 4 | 9.4.2.3, PUSCH 1-2 | Ericsson, Intel and Huawei (8x4)
 |  |  | Single and Multiple PMI report |  | ZTE
EVA5 | TM9 | 4x4 or 8x4 | 3 or 4 | 9.4.1.4, PUCCH 1-1 | Nokia
EVA5 | TM4 | 4x4 | 3 or 4 | 9.4.1.1, PUSCH 3-1 | Nokia

## Slide 7: Way Forward for 4Rx RI performance
Evaluate the RI testcases on next page

## Slide 8: RI
Propagation condition | Reporting | TM | Proposed new antenna configuration | Based on current 2Rx requirement section | Proposed by
EPA5 | PUCCH 1-1 | TM4 | 2x4 | 9.5.1.1 | Intel, Huawei, Nokia
EPA5 | PUCCH 1-1 | TM9 | 4x4 | 9.5.2.1 | Ericsson, Intel, Nokia