## Slide 1: Way forward on coexistence tests for LAA
Ericsson, Qualcomm
3GPP TSG-RAN WG4 Meeting #76bis R4-156924 Sophia Antipolis, France, 12 – 16 October, 2015

## Slide 2: Content
This way forward contains the following:
  Requirements related to LBT
  LBT tests
  Multi-node tests
  Time plan

## Slide 3: LBT requirements for LAA operations
Specify the following requirements in 36.104
  LBT BW: The LBT bandwidth will be 20MHz, as it is agreed so far.
  Energy detection thresholds: depends on RAN1
  Random back-off values: depends on RAN1
  Maximum channel occupancy time: depends on RAN1
  LBT measurement accuracy requirement: During a CCA slot, Base Station should sense the channel for at least X µsec. From this sensing, the Base Station should be able to assess whether the medium is busy or idle with at least Y% probability.

## Slide 4: LBT tests
Capability to perform Energy detection
  Includes performance of energy detection thresholds, LBT measurement accuracy tests, etc.
Channel access mechanism tests
  Depends on LBT parameters, e.g. random back-off time, maximum channel occupancy time, etc
The above tests will cover the requirements in previous slide
LBT tests will ensure that LAA coexistence targets are met and hence fair coexistence with Wi-Fi

## Slide 5: Multi-node tests
Multi-node test should test coexistence with
  other wireless systems using the spectrum, e.g. Wi-Fi, and
  other LAA operators operating in the spectrum
Can be initiated in performance part of the WI
Multi-node tests represent additional test compared to the essential LBT related tests

## Slide 6: Time plan
Following time plan can be followed:
Tests | Core part of WI (until December 2015) | Performance part of WI (until June 2016)
Capability to perform Energy detection | Minimum requirements are documented in 36.104 | Details of actual test procedures to be defined and documented in 36.141
Channel access mechanism tests | Minimum requirements are documented in 36.104 | Details of actual test procedures to be defined and documented in 36.141
Multi-node tests |  | Study of type of test and test procedure. Details of possible test procedures to be defined and documented in 36.141