## Slide 1: 3GPP TSG-RAN WG4 Meeting #79 Nanjing, China, 2016
Nokia, Ericsson, Huawei, DoCoMo
Way forward on NPRACH simulation assumptions
R4-164491

## Slide 2: Background
It is observed that significant gap exists between NPRACH detection performance and timing estimation performance.
  Ref: R4-164350, R4-164351

## Slide 3: Way Forward
Further study is needed to capture both timing estimation performance and missed detection performance for NPRACH requirements.
Companies are encouraged
  to provide simulation results based on the simulation assumptions and
  to provide inputs on the performance criterion for NPRACH, for example,
    X [%] of false alarm rate
    Y [%] of missed detection rate

## Slide 4: Simulation assumptions
It is FFS on the timing limits. Frequency offset for [TU1/EPA1] should be aligned to UE RF requirements on frequency offset. For the initial simulation, [200Hz] is assumed based on the current agreement on UE frequency offset.
Parameter | Values
Preamble format | 0
Number of Repetitions | 2, 8, 32
Number of Subcarriers | 12, [24]
Antenna configuration | 1 x 2
frequency offset | 0Hz (AWGN); [200]Hz ([TU1/EPA1])
Propagation channels | AWGN, [TU1,EPA1]
Detection performance | Missed detection rate (1%) with false alarm rate (0.1%)
Timing estimation | Timing error probability with limits 2.5us, [5us]