## Slide 1: Way forward on NB-IoT UE OOBB Range 3
Intel, MediaTek, ASTRI, Huawei, Hi-Silicon, Neul, [Nokia, Qualcomm, Vodafone, Telecom Italia, Sony …]
3GPP TSG-RAN WG4 Meeting #79 R4-164520 Nanjing, China, 22 – 27 May, 2016

## Slide 2: Background (1/2)
NB-IoT is targeting small size and low cost. It was noted that SAW-less receiver may be useful for low cost NB-IoT applications. In consequence out-of-band blocking (OOBB) requirement may need to reflect that. A SAW-less architecture will save PCB area and have lower cost.
In addition it was also noted that more stringent OOBB requirement will lead to lower phase noise requirement on LO, and lower phase noise requirement will lead to much more current consumption in synthesizer. Therefore, less stringent OOBB will also lead to lower power consumption.
Details on power consumption improvement, cost reduction, impact in performance were not available.
The following proposals were made:
  R4-163558 proposed Pinterference=-20dBm for NB-IoT UE OOBB range 3
  R4-164465 proposed Pinterference=-25dBm for NB-IoT UE OOBB range 3
  Other proposals have been to keep Pinterference=-15dBm for NB-IoT UE OOBB range 3

## Slide 3: Background (2/2)
NB-IoT frequency band can be categorized into two band groups:
Low frequency band group: Band 5, 8, 12, 13, 17, 18, 19, 20, 26, 28
DL frequency range: 734~960MHz,
High frequency band group: 1, 2, 3,66
DL frequency range: 1805~2200MHz

## Slide 4: Way forward on NB-IoT UE OOBB Range 3
Note 1: For operating bands which downlink band frequency range is 729 MHz <= f < 1 GHz the power level of the interferer (PInterferer) for Range 3 shall be modified to –[20] dBm for the frequency range which is bounded by FDL_low - [150]MHz of the lowest band that UE supports in frequency range 729 MHz <= f < 1 GHz, and FDL_high + [200]MHz of the highest band that UE supports in frequency range 729 MHz <= f < 1 GHz.
Note 2: For operating bands which downlink band frequency range is 1805 MHz <= f <= 2200 MHz the power level of the interferer (PInterferer) for Range 3 shall be modified to –[20] dBm for FInterferer > FDL_low – [200] MHz and FInterferer < FDL_high + [200]MHz
Note 3: For each one of above bands, the power level of the interferer (PInterferer) for Range 3 shall be -15 dBm outside corresponding frequency ranges indicated above.