## Slide 1: Way forward on eMTC UE demodulation and CSI requirements
Ericsson,[Huawei],[HiSilicon], [Qualcomm],[Samsung], [NTT DOCOMO]
3GPP TSG-RAN WG4 Meeting #79
Nanjing, China 23-27 May, 2016
R4-164608

## Slide 2: Simulation results alignment
Companies are encouraged to provide the updated simulation results for alignment.

## Slide 3: Reference receiver for alignment
Simulation results should be based on:
  For MPDCCH/PDSCH TM9 tests, non cross-subframe channel estimation
  Realistic frequency error tacking
  Modeling of the behavior of half-duplex FDD, e.g.,
    Reset the coherent channel estimation after the UL->DL gap

## Slide 4: Alignment of the PBCH simulation results
Alignment study consists of:
  Step 1: provide the simulation results for alignment without repetition under EPA1
  Step 2: provide the simulation results with repetition under EPA1
Refer to R4-164604 for the detailed simulation parameters

## Slide 5: Alignment of MPDCCH CE Mode A simulation results
Alignment study consists of:
  Step 1: provide the results with AWGN with repetition
    Number of repetitions: 1, 8, 16
  Step 2: provide the results with EPA5 with repetition
Refer to R4-164605 for the detailed simulation parameters
After the alignment, the number of repetition to be decided.

## Slide 6: Alignment of the PDSCH TM6 simulation results
Alignment study consists of:
  Step 1: provide the TM6 with fixed PMI simulation results for alignment
    PMI=0, without repetition
  Step 2: Provide the TM2 simulation results for alignment purpose
    Without repetition
  Step 3: provide the TM6 simulation results without repetition
    PMI feedback periodicity with PUCCH 1-1: [8ms]
Refer to R4-164606 for the detailed simulation parameters for alignment

## Slide 7: MPDCCH CE Mode B test case
Propagation channel:
  Propagation channel
    Two options: AWGN, ETU1
After the alignment, the number of repetition to be decided

## Slide 8: PDSCH demodulation requirement
CE Mode A TM9
  Set the maximum number of HARQ retransmission to 1
  SNR test point considering the sufficient MPDDCH decoding performance
    Option1: 0dB
    Option2: -6dB
    Option3: [-3dB] (between 0dB and -6dB)
  Coding rate
    Option1: 1/10 (TBS=152bits)
    Option2: 1/3 (TBS=504bits)
    Option3: Other coding rate is not precluded
  Number of repetitions
    Select the number which can satisfy the SNR test point

## Slide 9: PDSCH demodulation requirement
CE Mode B TM2
  Set the maximum number of HARQ retransmission to 1
  Propagation channel
    Two options: AWGN, ETU1
  Number of repetitions:
    Option1: Number to satisfy BLER=30% with the target SNR with QPSK, TBS=152bits
    Option2: Same or longer value than MPDCCH repetition.
      TBS size may need change

## Slide 10: CQI tests
CQI definition test
  Companies are encouraged to provide the simulation result in the next meeting in order to set the test points
  Refer to CR R4-164607 for the detailed parameters
Sub-band CQI test
  Companies are encouraged to analyze the test method and provide the simulation result
  Refer to R4-163588 for the detailed parameters
    Propagation channel changed to B.2.4 with [1Hz] of Doppler frequency