## Slide 1: WF on MUST Blind Detection Issues
MediaTek, …
3GPP TSG-RAN WG4 Meeting #79 Nanjing, China, 23rd-27th May 2016
Agenda Item: 7.21.2
R4-164625

## Slide 2: Way Forward
For MUST cases 1 and 2, blind detection on MUST interference existence is not reliable for MUST-near UE
  Signaling is required
  MUST interference presence/absence should be consistent among all of its scheduled PRBs
For MUST cases 1 and 2, Study blind detection feasibility of power ratio for MUST-near UE
  CRS TM : TM2, TM4 rank 1, TM4 rank 2
  DMRS TM : TM9 rank 1, TM9 rank 2
Power ratio examples can be reference in
  R1-165763, R1-165797

## Slide 3: Way Forward
For MUST case 3, further study blind detection feasibility on presence/precoder/modulation of interference UE in the following cases
  CRS-based TM with 2TX or 4 Tx when UE is scheduled with TM2 or TM4 rank 1
  DMRS-based TM with OCC2 DMRS or OCC4 DMRS when UE is scheduled with rank 1
  Further check if NAICS conclusions can be applied
Signaling is still beneficial for MUST case 3