## Slide 1: WF on Uncertainty distribution and values for common equipments used in EIRP/EIS test
R4-164720
Sumitomo Electric, NEC, Ericsson, Nokia, Huawei

## Slide 2: Background (1/2)
In the last meeting RAN4#78bis held in San Jose del Cabo, in order to efficiently work out the OTA test tolerance values, after online and offline discussion, the following was agreed and recorded in the RAN4#78bis RF chairman’s note.
--------------------------------------- Start of the citation --------------------------
Agreements:
1) All uncertainty budgets are only applicable for existing frequency bands defined in MSR.
  a. Uncertainty budget value for f <3 GHz
  b. Uncertainty budget value for f 3 - 4.2 GHz
2) Each purposed uncertainty budget should specify which is applies (either a or b)
3) Align the uncertainty value of the reference antenna used for calibration stage
4) Align the uncertainty distribution of each value between different test methods for the same uncertainty elementNetwork analyzer, power meters, or other equipment uncertainty, should align with a common value for different test methods taking into account dynamic range operation
5) Use signal generator uncertainty from 37.141 if no other information available
------------------------------------------------ End of the citation -------------------------------

## Slide 3: Background (2/2)
The common equipment used in all test methods that were identified during the offline discussion in the last meeting includes:
Power measurement equipment, like spectrum analyzer and power meter used at the EIRP measurement stage
RF signal generator used only at the EIS measurement stage
Network analyzer used at the calibration stage
Reference antenna used at the calibration stage
Companies proposed different uncertainty values on these equipments.

## Slide 4: Companies’ proposed standard uncertainties (σ) of Measurement Equipment
Company | Proposed σ Measurement equipment (dB) |  | Proposed distribution | Tdoc No.
 | f≦3GHz | 3GHz≦f<4.2GHz |  | 
Huawei | 0.35 | 0.35 |  | R4-164285, R4-164286
Ericsson | 0.135 | 0.135 | normal | R4-163902
Nokia | 0.34 | 0.34 |  | R4-162625
MVG *not general commercial equipment | 0.048 | 0.048 | normal | R4-162668
Kathrein | 0.1 | 0.1 |  | R4-163923, R4-163897
NEC | 0.23 | 0.35 | rectangular | R4-164340
SEI | 0.32 | 0.45 | normal | R4-163750

## Slide 5: Companies’ proposed standard uncertainties (σ) of Signal Generator
Company | Proposed σ Signal generator (dB) |  | Proposed distribution | Tdoc No.
 | f≦3GHz | 3GHz≦f<4.2GHz |  | 
Huawei | 0.5 | 0.5 |  | R4-164286
Ericsson | 0.4 | 0.4 | normal | R4-163903
Nokia | 0.2 | 0.2 |  | R4-162626
MVG | 0.5 | 0.5 | normal | R4-164410
Kathrein | 0.25 | 0.25 |  | R4-163923, R4-163897
NEC | 0.23 | 0.35 | rectangular | R4-164341
SEI | 0.32 | 0.47 | normal | R4-163749

## Slide 6: Companies’ proposed standard uncertainties (σ) of Network Analyzer
Company | Proposed σ Network analyzer (dB) |  | Proposed distribution | Tdoc No.
 | f≦3GHz | 3GHz≦f<4.2GHz |  | 
Huawei | 0.18 | 0.18 |  | R4-164285, R4-164286
Ericsson | 0.12 | 0.12 | Rectangular | R4-163902, R4-163903
Nokia | 0.05 | 0.05 |  | R4-162625, R4-162626
MVG | 0.18 | 0.18 | normal | R4-162668,R4-164410
NEC | 0.17 | 0.12 | Rectangular | R4-164340, R4-164341
SEI | 0.1 | 0.11 | normal | R4-164778,R4-163750

## Slide 7: Companies’ proposed standard uncertainties (σ) of Reference Antenna
Company | Proposed σ Reference antenna (dB) |  | Proposed distribution | Tdoc No.
 | f≦3GHz | 3GHz≦f<4.2GHz |  | 
Huawei | 0.215 | 0.215 |  | R4-164285, R4-164286
Ericsson | 0.14 | 0.14 | Exp. normal | R4-163902, R4-163903
Nokia | 0.23 | 0.23 |  | R4-162625, R4-162626
MVG | 0.215 | 0.215 | normal | R4-162668,R4-164410
Kathrein * values in the tdocs are 2σ | 0.25 | 0.25 |  | R4-163923, R4-163897
NEC | 0.29 | 0.17 | rectangular | R4-164340, R4-164341
SEI | 0.29 | 0.17 | rectangular | R4-164778, R4-163750

## Slide 8
Equipment | Proposed σ (dB) |  | Proposed distribution | Proposing companies
 | f≦3GHz | 3GHz≦f<4.2GHz |  | 
Measurement equipment | 0.12 | 0.41 | normal | Rohde & Schwarz, Keysight
Signal Generator | 0.46 | 0.46 | normal | 
Network Analyzer | 0.13 | 0.20 | normal | 
Test vendors’ proposed standard uncertainties (σ)
*These values were derived from datasheets of mid-tier to high-end signal generators, spectrum analyzers, and VNAs.
* The value of measurement equipment was derived from datasheet of spectrum analyzers.

## Slide 9: Way Forward (1/2)
The following uncertainty distribution and standard uncertainty (σ) values proposed by test vendors shall be adopted for the measurement equipment, signal generator, and network analyzer in all test methods to calculate the uncertainty budget.
 | Standard uncertainty σ(dB) |  | Distribution
 | f≦3GHz | 3GHz≦f<4.2GHz | 
Measurement equipment | [0.12] | [0.41]* | normal
Signal generator | 0.46 | 0.46 | normal
Network analyzer | 0.13 | 0.20 | normal
The following uncertainty distribution and standard uncertainty (σ) value for the reference antenna derived as the maximum of companies’ proposals shall be adopted in all test methods to calculate the uncertainty budget.
 | Standard uncertainty σ(dB) |  | Distribution
 | f≦3GHz | 3GHz≦f<4.2GHz | 
Reference antenna | 0.29 | 0.25 | Rectangular
*: This value is valid for equipment with frequency range up to 8GHz.
Test equipment vendors are requested to suggest a more suitable value for
frequency range up to 4.2GHz.

## Slide 10
Uncertainty of other contribution factors except for the above 4 common equipments shall be harmonized among supporting companies for every test method.
The uncertainty budget for every test method shall be resubmitted with the above harmonized uncertainty values.
Way Forward (2/2)