## Slide 1: 3GPP TSG-RAN WG4 Meeting #79 Nanjing, P.R.China, 23 – 27 May 2016
Huawei, Ericsson, [Qualcomm], [Intel]
Way forward on the burst transmission model for LAA demodulation
R4-164748

## Slide 2: Background
In RAN4#78 meeting, the burst transmission model is discussed and several options are listed as:
  Option 1: Explicitly model LBT transmission (Ericsson, R4-160367)
  Option 2: Design a repeated burst transmission pattern. pre-define 8 types of burst pattern, after the previous burst transmission, randomly decide to chose which burst type out of 8 types (Huawei, R4-160742)
  Option 3: Define DL burst transmission model based on Poisson arrival process. Number of subframes in a transmission burst is chosen uniformly from {4,5,6,7,8}. (QC, R4-160046)
  More input from other companies are highly welcome.
In RAN4#78bis meeting, WF R4-162754 was agreed with Option 1 and Option 2 listed.
In this WF, we give the updated Option 1 and Option 2.

## Slide 3: WF on the signal model (Option 1)
Determination of burst format
  Select the number of subframes randomly from {1,3,5,8} with equal probability
  If the number of subframes is equal to 1, set the subframe as full subframe, otherwise
    If initial partial subframe is supported by UE, select start symbol for initial subframe randomly from {0, 7} with equal probability. Otherwise, start symbol of initial subframe is always 0.
    If end partial subframe is supported by UE, select number of OFDM symbols in end subframe randomly from {6, 9, 12, 14} with equal probability. Otherwise, end subframe always has 14 OFDM symbols.

## Slide 4: WF on the signal model (Option 1)
For each transmitted/muted burst
  TE determines burst format
  TE generates a uniform random variable from [0, 1]
  If random variable is less than p=[0.5]
    If both end subframe of previous burst and initial subframe of new burst is full subframe, start burst transmission after deferring one subframe
    Otherwise, start transmission from the latest start symbol determined from the determined burst format
  Otherwise, mute burst transmission
    Muting duration is same as number of subframe for determined burst format

## Slide 5: WF on the signal model (Option 2)
Set the transmission cycle and burst pattern set:
  Set the cycle for a burst pattern to 40ms; Fix the TB size to 18SFs the per burst pattern; Design 2 patterns: {1, 8, 4, 5} and {2, 7, 3, 6} that covers all possible number of subframes.
Determine the burst format:
  Select one pattern randomly from 2 pattern sets: {1, 8, 4, 5} and {2, 7, 3, 6};
  Select the number of subframe randomly from {1, 8, 4, 5} or {2, 7, 3, 6};
  If the number of subframes is equal to 1, set the subframe as full subframe, otherwise
    If initial partial subframe is supported by UE, the start symbol for initial subframe is selected from {0, 7} with 1/2 probability to be sent with each burst transmission within the transmission cycle. Otherwise, start symbol of initial subframe is always 0.
    If end partial subframe is supported by UE, select number of OFDM symbols in end subframe randomly from {6, 9, 12} with 1/3 probability to be sent with each burst transmission within the transmission cycle. Otherwise, end subframe always has 14 OFDM symbols.

## Slide 6: WF on the signal model (Option 2)
Burst Transmission
  TE selects the transmission start point randomly from the four 10 subframes in order;
  Defer at least one slot and less than 20ms before each transmission;
  If the continuous transmission period exceeds 8ms, start the burst transmission by deferring one subframe;
  Repeat the above steps for [10000]ms.

## Slide 7: WF on the signal model
In the next meeting, RAN4 will make final decision on which option will be used for demodulation.