## Slide 1: 3GPP TSG-RAN WG4 Meeting #79 Nanjing, P.R.China, 23 – 27 May 2016
Huawei, HiSilicon, Ericsson, Qualcomm, Intel, LG electronics
Way forward on LAA demodulation performance
R4-164749

## Slide 2: Background
RAN4#78 Malta meeting, WF R4-1611862 was agreed, but still many open issues left.
As per the further discussions in RAN4#78bis, WF R4-162753 was agreed, progress was made and still some opens issues left.

## Slide 3: General
        Introduce new PDSCH tests in CA mode for Rel-13 LAA with
  1 PCell with 1.4MHz ~20MHz BW + 1 LAA SCell both with 20MHz BW;
  Both FDD PCell and TDD PCell should be covered;
  Both PCell and LAA SCell should be verified.
        Tests for full, initial and ending partial SFs
  Test Scenarios to be defined:
    Test Scenario 1: full subframe only;
    Test Scenario 2: full subframe + ending partial subframe;
    Test Scenario 3: Initial partial subframe + full subframe;
    Test Scenario 4: Initial partial subframe + full subframe + ending partial subframe.
  RAN4 will define different tests for different capabilities. UEs will be tested based on its capability with the understanding that one test scenario is applied for a specific UE.
  It is also subject to RAN1 decision whether ending partial subframe will be mandatory or optional.

## Slide 4: General
        (e)PDCCH performance verification:
  Option 1: Explicitly
  Option 2: Implicitly verify the (e)PDCCH performance via PDSCH tests
  Note: Companies to bring simulation results to assess PDCCH and PDSCH performance for potentially wrong UE implementation.
        MBSFN subframe configuration:
          Option1: MBSFN is configured in subframes 4 and 9 for DMRS-based transmission mode
          Option 2: Not configure MBSFN
        DRS configuration: with DMTC period 80ms

## Slide 5: General
Frequency offset and timing error, and synchronization:
  Frequency offset and timing error of LAA Scell should be set relative to Pcell
    Option 1: [750]Hz, [30.26]μs
    Option 2: 200 Hz, 3 us
Reference receiver:
  MMSE-IRC receiver
    With practical frequency and timing tracking
    With practical detection

## Slide 6: PDSCH test cases and parameters
For PCell, to save the simulation efforts, reuse the following existing test cases:
  TM3 rank-2, EVA70, 2x2 Low, 16QAM ½
  TM4 rank-2, EVA5, 4x2 Low, 16QAM ½
For the LAA SCell
  Option 1: TM4 4x2, TM9 2x2
  Option 2: TM3 2x2, TM4 4x2, TM9 2x2

## Slide 7: Test metric
Reuse relative throughput (TP)
    70% TP as starting point.
    Relative throughput is the ratio of the throughput values per component carrier to the sum of the nominal maximum throughput values per component carrier.
      Nominal maximum throughput is
Nominal Max throughput = (Total data transmitted)/(Total time used for transmission)
Burst transmission model
  Details please refer to R4-164748

## Slide 8: Thanks