## Slide 1: 3GPP TSG-RAN WG4 Meeting #79 Nanjing, P.R.China, 23 – 27 May 2016
Huawei, HiSilicon, Ericsson, Qualcomm, Intel, LG electronics
Way forward on LAA CSI requirements
R4-164750

## Slide 2: Background
RAN4#78 Malta meeting, WF R4-1611862 was agreed, but still many open issues left.
As per the further discussions in RAN4#78bis, WF R4-162753 was agreed, progress was made and still some opens issues left for CSI test.

## Slide 3: CSI test
CQI feedback mode:
  Aperiodic CQI test
  Periodic CQI test is for further decision
One CSI test for CRS based transmission scheme and one CSI test for DMRS based transmission scheme for the corresponding CQI feedback mode
Transmission mode
  Baseline: TM3 (CRS based CSI measurement) and TM9 (CSI-RS based)
    If any issues is identified for TM3, TM2 may be selected
Test methodology
  Two power levels

## Slide 4: Test setup for aperiodic CSI test
Channel model
  Static channel model is used
Antenna configuration
  2x2
Feedback mode
  TM3 [PUSCH 3-0]
  TM9 PUSCH 3-1
Test metrics
  Option1:
    CQI distribution
    BLER metric
    Delta CQI for the feedback for different power level
  Option 2: Delta CQI for the feedback for different power level
        DRS configuration: DMTC period 80ms

## Slide 5: Test setup for aperiodic CSI test
Burst model
  Please refer to R4-164748 with the following exceptions
    No partial subframes
    Only randomly select two burst lengths from {3,8}
Transmission model
  SNR during DL transmission bursts is changed randomly either by [0]dB or [6]dB with equal probability
Test method:
  TE keeps track of CSI reporting separately for SNR [0]dB and [6]dB boosting subframes and applies that to PDSCH transmission with corresponding SNR value

## Slide 6: Thanks