## Slide 1
3GPP TSG-RAN WG4 #79
Nanjing, China, 23-27 May,2016
Agenda item: 7.13.3
LG Electronics
WF on RRM core requirement for V2V
R4-164751

## Slide 2: WF on analysis of RRM core requirement
ProSe UE transmission timing
  eNB as time reference
    TE : Existing requirement can be reused
  GNSS as time reference
      Requirements for timing misalignment between GNSS based and eNB based timing should be discussed after RAN1 decision
    TE = +/- 12Ts
  SyncRef UE as time reference
    FFS
Selection/Reselection of ProSe Sync.Reference
  To GNSS
    FFS
  To SyncRef UE
    Need to evaluate with new DMRS under moderate & high speed
    Encourage companies to provide simulation results in RAN4#80

## Slide 3: WF on analysis of RRM core requirement
Initiation/Cease of SLSS transmission
  eNB based SLSS
    Enhancement of DRX RSRP measurement requirements for V2V is de-prioritized
  GNSS based SLSS
    It should be discussed after RAN1 decision
  SyncRef based SLSS
    Need to evaluate with new DMRS under moderate & high speed
    Encourage companies to provide simulation results in RAN4#80
Measurements for ProSe in Any Cell Selection State
  Cell detection
    Consider to update cell detection time due to high speed based on analysis
Interruption
  Encourage companies to study on interruption impact due to V2V UE TX capability
Measurement of congestion control & collision avoidance
  Shall be discussed based on RAN1 agreement