## Slide 1: 3GPP TSG-RAN WG4 Meeting #79 Nanjing, China, 23rd – 27th May, 2016
Intel, Samsung
Network-assisted signalling for high speed scenarios
R4-164757

## Slide 2: Background
Currently, RAN4 identified that legacy channel estimation and RRM measurement needs to be improved for HST support.
It is importance for a UE to accurately know about HST environments for enabling HST UE behaviours.
Intentions of signalling introduction are
  1. to prevent regular UEs from enabling HST UE behaviours
  2. to utilize effectively HST UE functions in HST running circumstances

## Slide 3: HST RRM
  HST UE need only measure the cell in the limited neighbor cell list in HST.
  Signaling 1 : limited neighbor cell list
Network provides limited neighbor cell lists for HST UE cell measurement.
  - Option 1 : reuse legacy signaling by revising signaling usecase (e.g. “IntraFreqNeighCellList or InterFreqNeighCellList” and “CellsToAddMod” for RRC_IDLE and RRC_CONNECT status respectively)
  - Option 2 : Introduce a new signaling for HST RRM

## Slide 4: HST Demod
A HST UE takes corresponding actions based on network signalling.
  Possible Signallings :
  Signalling 1 : High speed train (HST) is running on HST rail at high speed
  Signalling 2 : Signalling at location of changing SFN such as cell edge of SFN RRHs
  Signalling 3 : Unidirectional or Bidirectional SFN
Companies provide preferences on HST signaling in the next meeting.

## Slide 5: Signaling and Test method
HST signaling is cell specific.
HST UE tests are conducted with a given HST signaling
HST UE performance robustness is FFS ( i.e. performances when HST CE is applied for low Doppler channels )
  HST UE needs blind detection for HST scenarios based on the signaling.