## Slide 1: WF on MUST Blind Detection Issues
MediaTek, Samsung, CMCC , Huawei, HiSi, Nokia, Intel
3GPP TSG-RAN WG4 Meeting #79 Nanjing, China, 23rd-27th May 2016
Agenda Item: 7.21.2
R4-164759

## Slide 2: Way Forward
For MUST case 1 and 2, error in interference existence detection will lead to 100% BLER of the PDSCH
For MUST cases 1 and 2, study blind detection feasibility of power ratio for MUST-near UE
  CRS TM : TM2, TM3, TM4 rank 1, TM4 rank 2
  DMRS TM : TM9 rank 1, TM9 rank 2
Power ratio examples can be referenced in
  R1-165763, R1-165797

## Slide 3: Way Forward
For MUST case 3, further study blind detection feasibility on presence/precoder/modulation of interference UE in the following cases
  CRS-based TM with 2TX or 4 Tx when UE is scheduled with TM2 or TM4 rank 1
  DMRS-based TM with OCC2 DMRS or OCC4 DMRS when UE is scheduled with rank 1
  Further check if NAICS conclusions can be applied
Signaling is still beneficial for MUST case 3

## Slide 4: Way Forward
For all MUST cases, the feasibility study should take into account at least the following metrics
  Detection rates of parameters
  Throughput loss compared with the case with genie information provided
  UE implementation complexity