## Slide 1: WF on MUST Simulation Assumptions
MediaTek, Samsung, CMCC, Huawei, HiSi, Nokia, Intel
3GPP TSG-RAN WG4 Meeting #79 Nanjing, China, 23rd-27th May 2016
Agenda Item: 7.21.2
R4-164760

## Slide 2: Background
This WF provides the simulation assumptions for RAN4 to identify feasibility on the parameter blind detection in the next meeting.

## Slide 3: Way Forward Common simulation parameters
Parameter for target (near) UE | Value
Bandwidth | 10MHz
Cyclic prefix | Normal
Propagation channel | EVA5, ETU5
Number of OFDM symbol for control region | 3
Subframes with PDSCH | #1, 2, 3, 4, 6, 7, 8 and 9
Number of PRBs of PDSCH | Baseline: 50
Rank | Baseline: 1
HARQ | Disabled
Parameter on target UE demodulation | Value
Number of PRB used for one decision | Baseline: 1 Options: 1 RBG, 1 subband, full band
Number of REs used in a PRB for blind detection | To be specified in the contribution
Detection algorithm | To be specified in the contribution
Channel/noise estimation | Non-ideal
Demapper algorithm | Reduced ML, others are not precluded

## Slide 4: Way Forward simulation parameters for MUST cases 1 and 2
Parameter for target (near) UE | Value | 
 | CRS-based TM | DMRS-based TM
Frame structure | FDD | 
Antenna configuration | 2x2 ULA low correlation | 
Cell-specific reference signals | Antenna ports 0,1 | 
Transmission mode | TM2, TM3, TM4 | TM9
Precoding | Random with Granularity of 50 PRBs | 
CSI reporting | Disabled | 
MCS of near UE | QPSK: 0 16QAM: 10 64QAM: 17 Other values are not precluded | 
Modulation of far UE | QPSK | 
TX EVM | 6% | 
MuST parameters to be blindly detected or signaled | existence and power ratio | 

## Slide 5: Way Forward simulation parameters for MUST case 3
Parameter | Value | 
 | CRS-based TM | DMRS-based TM
Frame structure | FDD | TDD
Antenna configuration | 2x2 ULA low correlation 4x2 ULA low correlation | 4x2 ULA low correlation 8x2 Xpol high correlation
Cell-specific reference signals | Antenna ports 0,1 Antenna ports 0,1,2,3 | Antenna ports 0,1
Transmission mode | TM4 | TM9
Number of interference UEs | 1 | 1 with (i) OCC-2 or (ii) OCC-4 Other options are not precluded.
Resource allocation of interference UE | Full band | 
MCS of target UE | Fix MCS | 
Modulation order of interference UE | Random | 
Precoding of target UE | Follow UE’s wideband PMI report with reporting mode 1-1 | 
Precoding of interference UE | Random with granularity of 1 PRB. Other options are not precluded. | 
TX EVM | 6% | 
MuST parameters to be blindly detected or signaled | existence, precoder, modulation order, power allocation | existence, DMRS port and modulation order