## Slide 1: WF on remaining details for eD2D demodulation requirements
Qualcomm, Intel
R4-164762
3GPP TSG-RAN WG4 Meeting #79
Nanjing, China, May. 23rd – May. 27th, 2016

## Slide 2: Background
Agreements from RAN4 #78:
  No new demodulation performance requirement test needed for UE-NW relays.
  No new demodulation performance requirement test needed for Group priority enhancement.
Agreements from RAN4 #78bis main session:
  Do not define new UE demodulation test case to verify Inter Frequency and Inter PLMN D2D Discovery.
  Introduce additional SDR tests with active Sidelink to verify no impacts on the CA DL performance in case of D2D Communication.
    For CA capable UE, UE only needs to pass the CA SDR tests.
Open issues:
  Demodulation performance for OOC Discovery
  Test for WAN SDR + active Sidelink Discovery to verify impact to WAN
  Clarifications on applicability of tests with Rel-12 SLSS and Rel-13 SLSS

## Slide 3: Proposals
Proposal 1: No new test for WAN SDR with active Sidelink Discovery is needed.
Proposal 2: Introduce a new demodulation performance test needed for OOC discovery.
Proposal 3: No new D2D Discovery demodulation performance tests needed due to multicarrier supported.
Proposal 4: RAN4 assumes the following understanding for Rel-12 SLSS (disc-SLSS-r12) and Rel-13 SLSS (discPeriodicSLSS-r13) UE capabilities
  UE indicates disc-SLSS-r12 for support of SLSS Tx and Rx for the purpose of inter-cell discovery.
  UE indicates discPeriodicSLSS-r13 for support of periodic SLSS Tx (in-coverage or out-of-coverage) and SLSS Rx (for the purpose of out-of-coverage discovery Rx).
Proposal 5: RAN4 assumes the following test case applicability
  UEs indicating discPeriodicSLSS-r13 and disc-SLSS-r12 capabilities are supposed to pass inter-cell discovery test cases (i.e. Multiple timing reference test).
  UEs indicating discPeriodicSLSS-r13 and no disc-SLSS-r12 capabilities are not supposed to pass inter-cell discovery test cases (i.e. Multiple timing reference test).