## Slide 1: Way forward on UE performance requirements for FD-MIMO
Samsung, [Qualcomm],[MediaTek], [Ericsson],[Intel],[LGE],[Huawei]
3GPP TSG-RAN WG4 Meeting #79
Nanjing, China, 23th – 27th May 2016
R4-164859

## Slide 2
  DMRS configuration for target UE
  Fixed as port 11, nSCID=0, OCC=4
Number of interference port
  1 port with nSCID= 0,OCC =4
Interference port selection: randomized interference port between port{7, 8,13}
  Option 1: per TTI per RBG basis
  Option 2: per TTI per RB basis
  Option 3: per TTI basis
  Decide set-up in next RAN4 meeting
Detailed test parameters
  Reusing existing test parameters for FRC, propagation channel, antenna correlation, and beam-forming mode as specified in 36.101 8.3.1.1 Test 2
Performance requirements:
  Bring simulation results and deciding performance requirements for FDD mode and TDD mode in next RAN4 meeting.
PDSCH demodulation test

## Slide 3
Test Metric
  Reusing existing 8Tx PMI test metric: , is 90%] of the maximum throughput obtained at using the precoders configured according to the UE reports, and is the throughput measured at with random precoding.
Test applicability for CSS configuration:
  Defining performance requirements which applicable for all the CSS configurations. For each test case, select corresponding CSS configuration based on UE capability
    Random select one of codebook configuration value from UE supported codebook configurations
Performance requirements:
  FDD mode: single PMI [2.5], multiple PMI [2.5]
  TDD mode: Bring simulation results for both single PMI and multiple PMI test case and deciding performance requirements for TDD mode in next RAN4 meeting.
Class A PMI test cases

## Slide 4
Test applicability
  In Rel-13 time frame, only introduce test case under TM9 with 1 CC
  Introduce a subset of test cases with different (K, Nmax)
    At least including (K,Nmax )= (2,8), FFS for (8,64), other possible configurations are FFS
    The detailed applicability rule based UE capability is FFS
Test methodology
  Option 1: One throughput test with single CSI-RS resource and another throughput test with multiple CSI-RS resources.
    Alt.1: Check both CRI statistics and throughput ratio between following CRI and fixed CRI.
    MCS selection and PMI selection FFS
  Other options will not be precluded.
Beamforming model
  Option 1: Dynamic power scaling
    with A = [0.8],B=1 (As example)
  Option 2: CSI-RS resource specific beamforming and beam steering channel model
Class B K>1 CRI test case (RAN4#78bis agreements)

## Slide 5
Per UE: 1-bit indicating whether to support the alternative codebook (for K=1 case only)
Per UE per band per band-combination P times (for 1, …, P CSI processes)
  3-bit Kmax (Kmax = {2,3,4,5,6,7,8})
  1-bit Nmax configuration (2 possible values) per K value, from K=2,…, Kmax. The two Nmax values for each K is given as follows
CRI capability RRC signaling in RAN2 (information)
K | 2 | 3 | 4 | 5 | 6 | 7 | 8
Nmax | {8,16} | {8,16} | {8,32} | {16,32} | {16,32} | {16,32} | {16,64}

## Slide 6
Test applicability
  Introduce a subset of test cases with different (K, Nmax)
    At least consider the following configurations
    FFS if additional test cases are needed
  Test case applicability based on UE capabilities is FFS
    Option1: Based on UE capability, each UE pick up one configuration to pass with following applicability rule to determine {K, Nmax} :
      If UE supporting (K,Nmax) = (8,64), then pass test with (8,64)
      else if UE supporting (K,Nmax) = (4,32) then pass test with (4,32)
      else if UE supporting (K,Nmax) = (2,16) then pass test with (2,16)
      Other wise UE pass test with (2,8)
    Other options not excluded
Test applicability
For Class B K>1 CRI test case
Test number | #1 | #2 | #3 | #4
(K, Ntotal) | (2,8) | (2,16) | (4,32) | (8,64)

## Slide 7
Test Methodology
  One throughput test with single CSI-RS resource and another throughput test with multiple CSI-RS resources.
    Check both CRI statistics and throughput ratio between following CRI and fixed CRI.
VRC test or FRC test
  FRC test with fixed rank, MCS (16QAM ½ Rank1)
    Option 1: Fixed PMI for both following CRI and fixed CRI
    Option 2: Following PMI for both following PMI CRI and fixed CRI following CRI, fixed PMI for fixed CRI
Beam-forming model
  Option 1: Dynamic power scaling method (Baseline)
    Log scale with A = [5] dB, B = [0] dB
    fs is FFS
    k = 0,1,2,…,K-1
  Option 2: Fixed Power scaling method
Detailed test parameters
  Further discuss detailed test set-up through RAN4 email reflector so that all the companies can run the simulations for the next RAN4 meeting to speed up the progress.
Class B K>1 CRI test case

## Slide 8
Test Point: 70% of maximum throughput with following PMI
MIMO channel correlation
  ULA Low EPA5Hz 8*2 for TDD
  ULA Low EPA5Hz 4*2 for FDD
MCS & Rank: 16QAM ½ rank1
Performance requirements
  Bring simulation results for both FDD and TDD mode and deciding performance requirements in next RAN4 meeting
Class B K=1 PMI test cases with PMI-config =1

## Slide 9
Test metrics
  Reusing existing static CQI test metric i.e. Reporting spread of CQI value + BLER requirements
  Test Set-up for Channel measurement restriction test
  Reusing test parameters for existing TM9 static CQI test as specified inTS36.101 9.2.3 with below modification:
    Adjusting transmitted power in even CSI-RS sub-frames, Transmitted power imbalance between even CSI-RS sub-frames and other sub-frames is TBD
      [ -12dB -9dB] for further down-selection
      Make decision for value in next RAN4 meeting based on companies simulation results
    Scheduled PDSCH will skip even CSI-RS sub-frame
    CQI reported based on odd CSI-RS sub-frames
  Test Set-up for Interference measurement restriction test:
  Reusing test parameters for existing TM10 static CQI test as specified in TS36.101 9.2.4 with below modification:
    Adjusting TP2 transmission power in even CSI-RS/CSI-IM sub-frames, transmitted power imbalance between even CSI-RS sub-frames and other sub-frames (for TP2) is TBD
      [6dB 9dB 12dB ] higher than other sub-frames
      Make decision for value in next RAN4 meeting based on companies simulation results
    Scheduled PDSCH will skip even CSI-RS sub-frames
    CQI reported based on odd CSI-RS sub-frames
MR test

## Slide 10
Simulation assumption for PDSCH demodulation test (For information)
parameter |  | Unit | Test X
Downlink power allocation |  | dB | 0
 |  | dB | 0 (Note 1)
 |  | dB | -3
System Bandwidth |  | MHz | 10
Beamforming model |  |  | Annex B.4.1
MIMO channel |  |  | EPA5Hz, 2*2 Low
Cell-specific reference signals |  |  | Antenna ports 0,1
CSI reference signals |  |  | Antenna ports 15,…,18
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  | Subframes | 5 / 2
CSI reference signal configuration |  |  | 3
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap |  | Subframes / bitmap | 3 / 0001000000000000
at antenna port |  | dBm/15kHz | -98
Symbols for unused PRBs |  |  | OCNG (Note 4)
Number of allocated resource blocks (Note 2) |  | PRB | 50
Rel-13-DMRS-table |  |  | Yes
MCS and Rank |  |  | 64QAM 1/2 Rank1 R.50 FDD
Simultaneous transmission |  |  | Yes
DMRS configuration for input signal |  |  | fixed as port 11, nSCID=0, OCC=4
DMRS configuration for interfering signal |  |  | 1 port with nSCID= 0,OCC =4
Interfere port selection |  |  | nterference port selection: randomized interference port between port{7, 8,13} Option 1: per TTI per RBG basis Option 2: per TTI per RB basis Option 3: per TTI basis
PDSCH transmission mode |  |  | 9

## Slide 11
Simulation assumption for CRI test (For information)
Parameter | Unit | Test 1 ((K,N)=(2,8)) | Test 2 ((K,N)=(2,16)) | Test 3 ((K,N)=(4,32)) | Test 4 ((K,N)=(8,64))
Bandwidth | MHz | 10 | 10 | 10 | 10
Transmission mode |  | 9 | 9 |  | 
Propagation channel |  | EPA5 | EPA5 | EPA5 | EPA5
Precoding granularity (only for reporting and following PMI) | PRB | 50 | 50 | 50 | 50
Correlation and antenna configuration |  | 4x2 XP High | 8x2 XP High | 8x2 XP High | 8x2 XP High
PMI adaptation |  | Option 1: Fixed PMI Option2: Following PMI |  |  | 
Cell-specific reference signals |  | Antenna ports 0,1 | Antenna ports 0,1 | Antenna ports 0,1 | Antenna ports 0,1
eMIMO-Type |  | Class B | Class B | Class B | Class B
Number of NZP-CSI resources (K) |  | 2 | 2 | 4 | 8
NZP-CSI-RS-ID-List |  | {0,1} | {0,1} | {0,1,2,3 } | {0,1,2,3,4,5,6,7}
legacyCSRList |  | {0,0} | {0,0} | {0,0,0,0} | {0,0,0,0,0,0,0,0}
CSI reference signal configuration List |  | {0,1} | {0,1} | {0,1,2,3 } | {0,1,2,3,0,1,2,3}
Number of CSI-RS ports (Nk) |  | {4,4} | {8,8} | {8,8,8,8} | {8,8,8,8,8,8,8,8}
CSI-RS-SubframeConfig List |  | {1,1} | {1,1} | {1,1,1,1} | {1,1,1,1,2,2,2,2}
CodeBookSubsetRestriction with ID=0 |  | Note2 | Note 3 | Note 3 | Note 3
Reporting mode |  | PUSCH 3-1 | PUSCH 3-1 | PUSCH 3-1 | PUSCH 3-1
Reporting interval | ms | 5 | 5 | 5 | 5
CRI Delay | ms | 8 | 8 | 8 | 8
PMI delay | ms | 8 | 8 | 8 | 8
Measurement channel |  | 16QAM 1/2 | 16QAM 1/2 | 16QAM 1/2 | 16QAM 1/2
Rank Number of PDSCH |  | 1 | 1 | 1 | 1
Scheduled PDSCH SFs |  | SF 0,2,3,4,7,8,9 | SF 0,2,3,4,7,8,9 | SF 0,2,3,4,7,8,9 | SF 0,3,4,8,9
Max number of HARQ transmissions |  | 4 | 4 | 4 | 4
Redundancy version coding sequence |  | {0,1,2,3} | {0,1,2,3} | {0,1,2,3} | {0,1,2,3}
Note 1: For following PMI approach, beam steering will applied to MIMO channel as specified in TS 36.101 B.2.3A.4. For fixed PMI approach, no beam steering in MIMO channel. Note 2: Under 4Tx, for following PMI:0x0000 0000 0000 FFFF 0000 00FF; for fixed PMI: 0x0000 0000 0000 0001 0000 0001 Note 3: Under 8Tx, for following PMI: 0x0000 0000 001F FFE0 0000 0000 FFFF; for fixed PMI: 0x0000 0000 0000 0010 0000 0000 0001 |  |  |  |  |