## Slide 1: Way forward on testing methodologies for eMTC
Ericsson, Qualcomm Incorporated, Nokia
3GPP TSG-RAN WG4 Meeting #79
Nanjing, China 23-27 May, 2016
R4-164887

## Slide 2: Testing Methodology for RLM
Radio link monitoring for CEModeB
  Problem: no CQI reporting is supported for Cat-M1 UE in CEModeB. Hence, RLM cannot be tested using existing testing methodology.
  Following options are under consideration:
    Option 1: Periodic serving cell RSRP measurement reporting
    Option 2: Periodic/continuous PUSCH scheduling
    Option 3: Use re-establishment to verify UE RLF status
    Other options are not precluded
    Based on the input and discussions, the necessity of the test will be discussed at RAN4#80.

## Slide 3: Testing Methodology for Timing related Test Cases
UE Timing related tests:
  UE Transmit Timing requirements Cat-M1 UE in CEModeB.
  UE Timing Advance Adjustment Accuracy Test in CEModeB
Problem: No SRS transmissions in CEModeB.
Following options are under consideration:
  Option 1: Using random access transmission
  Option 2: Using PUCCH/PUSCH transmission
  Other options are not precluded
Companies are to provide input on testing methodology for UE transmit timing requirements.
Based on the input and discussions, the necessity of the test will be discussed at RAN4#80.