## Slide 1
3GPP TSG-RAN WG4 #79
Nanjing, China, 23-27 May,2016
Agenda item: 7.13.3
LG Electronics
WF on RRM core requirement for V2V
R4-163693

## Slide 2: WF on analysis of RRM core requirement
Ran4 don’t specify reception requirement of GNSS and it is left on UE implementation.
  Selection/Reselection to GNSS
  Initiation/Cease GNSS based SLSS
Ran4 specify transmission requirement related to GNSS.
  TA(Timing advance), TE(Timing Error)
Ran4 consider RS structure of RAN1 working assumption to complete RRM core requirement in time of V2V WI.
Ran4 consider the high priority of SL TX over WAN TX for interruption requirement
Ran4 will complete RRM core requirement in RAN4#80 based on slide 3 & 4.

## Slide 3: Agreement of RRM core requirement
 |  |  | Reuse | New requirement | Not necessary | Comment
ProSe UE transmission timing (TA, TE) | IC | eNB | O |  |  | 
 |  | GNSS |  | O |  | TA=TBD(need Ran1 decision), TE=24·Ts
 |  | GNSS-based UE |  |  | O | Depending on Ran1
 | OoC | GNSS |  | O |  | TA=0·Ts,TE=24·Ts
 |  | GNSS-based UE | O |  |  | TA=0·Ts, TE=24·Ts
 |  | Legacy PC-5 UE | O |  |  | 
Selection/Reselection of ProSe Sync. Reference (Tdetect,SyncRef) | IC | eNB |  |  | O | 
 |  | GNSS |  |  | O | UE implementation
 |  | GNSS-based UE |  |  | O | Depending on Ran1
 | OoC | GNSS |  |  | O | UE implementation
 |  | GNSS-based UE | O |  |  | Need to consider drop rate
 |  | Legacy PC-5 UE | O |  |  | Need to consider drop rate
Initiation/Cease of SLSS Transmission (Tevaluate,SLSS) | IC | eNB based SLSS | O |  |  | Limit low DRX cycle regarding high speed
 |  | GNSS based SLSS |  |  | O | UE implementation
 |  | GNSS based UE based SLSS |  |  | O | Depending on Ran1
 | OoC | GNSS based SLSS |  |  | O | UE implementation
 |  | GNSS based UE based SLSS | O |  |  | Depending on Ran1 Need to consider new RS & high speed
 |  | Legacy PC-5 UE | O |  |  | Need to consider new RS & high speed

## Slide 4: Agreement of RRM core requirement
 |  |  | Reuse | New requirement | Not necessary | Comment
Measurements for ProSe in Any Cell Selection State | OoC | Cell identification | O |  |  | 
Interruption to WAN | RRC_IDLE | PDC | O |  |  | 
 | RRC_CONN. | PDC config. | O |  |  | 
 |  | During PDC | O |  |  | 
 |  | During PDC with comm.Gap(Tx) |  | O |  | Similar as PDD with transmission gaps
Interruption to PC-5 | IC |  |  |  | O | eNB is manageable
Measurement for sensing resource allocation | IC/OoC |  |  |  | O | Postpone to next V2X
PDC : ProSe Direct Communication
PDD : ProSe Direct Discovery