## Slide 1: Blind Detection Conclusions on MUST Case 1 and 2
MediaTek
3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22nd -26th August 2016
Agenda Item: 8.19.2
R4-165133

## Slide 2: Way Forward
In CRS-based TMs
  Blind detection on interference existence is not feasible
    The degradation due to existence detection error is significant for either OMA to NOMA or NOMA to OMA.
    Practical blind detection algorithms cannot achieve acceptable detection rate for both 1-layer and 2-layer in CRS-based TMs.
  Given the signaling of interference existence, the worst throughput degradation at BLER 10% of ideal performance due to blind detection on power ratio is
    < 1% in QPSK,
    < 5% in 16QAM, and
    10~20% in 64QAM.
  Additional UE computation complexity is required.

## Slide 3: Way Forward
In DMRS-based TMs
  If near and far UEs share the same DMRS port(s)/sequence(s), the conclusions in CRS-based TM can be directly applied.
  If near and far UEs do not share the same DMRS port/sequence, and their DMRSs are power scaled by their own power ratios
    Blind detection on Interference existence is feasible in terms of the throughput degradation
    The worst throughput degradation at BLER 10% of ideal performance due to blind detection on power ratio is
      < 1% in QPSK and 16QAM
      < 5% in 64QAM
  Additional UE computation complexity is required.