## Slide 1: Way forward on NB-IoT aggregate power control
Nokia
R4-166638

## Slide 2: Background
During RAN4#80 NB-IoT aggregate power control was dicussed [1] and two possible methods for defining the requriement was mentioned.
Define aggregate power control requirement such way that it covers the 256 ms max transmission period or shorter but requirement does not include a gap in transmission
Define aggregate power control requirement such way that it extends over the gap to ensure that accuracy is kept also when gap in transmission occurs.
[1] R4-165410, NB-IoT aggregate power control, Nokia

## Slide 3: Discussion
During the offline discussion it was concluded that if there is a transmission gap larger than 20 ms then Absolute power tolerance applies as defined in 6.3.5.1. Note: for NB-IoT E-UTRA absolute power tolerance applies. Hence first transmission after UCG shall fullfill absolute power tolerance requirement.
In conclusion Option 1 seems to be only possibility to define aggregate power tolearace for NB-IoT.
From 36.521 we can see the test patters to E-UTRA
From: 36.521: E-UTRA requirement consists of 5 consecutive transmissions separated by 4 ms in time. Measurement is done on power of 5 consecutive transmissions to verify the UE transmitted power is maintained within 21 ms. The transient periods of 20us are excluded from the power measurement.

## Slide 4: Way forward
Option 1 From [1] was chosen for basis of NB-IoT aggregate power control requriement.
Comppanies will provide detailed proposals for test pattern and for the requirement for RAN4#80bis.