## Slide 1: WF on measurement gap enhancement
Intel,
3GPP TSG-RAN WG4 Meeting #80 R4-166809
Gothenburg, Sweden, 22 - 26 Aug 2016, 2016

## Slide 2: Shorter MGL for synchronous operations
Shorter MGL configurations
  MGL: single MGL is defined (3ms or 4ms)
    Considering 4ms MGL makes the overall gain marginal, interested companies are encouraged to provide justification on MGL=4ms proposal.
  MGRP: two MGRP should be defined, i.e. 40ms and 80ms
Short gaps and legacy gaps are not mixed for both per-CC and per-UE based measurement gap configurations
RAN4 will send LS to RAN2 on the related agreements

## Slide 3: NCSG and interruption control
NCSG configurations for legacy gap for single carrier, CA and synchronous DC
  VIL-ML-VIL: 1ms-4ms-1ms (DL) and 1ms-4ms-2ms(UL)
  VIRP: 40ms and 80ms
NCSG configurations for other scenarios (e.g. async. DC) are FFS
NCSG configurations for short MGL are FFS
RAN4 will send LS to RAN2 on the related agreements

## Slide 4: Per-CC based measurement gap configuration
Per-CC based measurement gap can be configured based on existing measurement gap patterns (i.e. Gap Pattern Id 0 or 1) or the gap patterns with shorter MGL
  Short gaps and legacy gaps cannot be mixed for per-CC based measurement gap configurations
Per CC, measurement gap may or may not be configured
It is FFS if lower density measurement gap configurations are defined or not
RAN4 will send LS to RAN2 on the related agreements