## Slide 1: 3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22 - 26 Aug, 2016
Huawei, HiSilicon,[Samsung],[Ericsson],[Qualcomm],[Samsung]…
Way forward on NB-IoT transmission signal pattern for NPDCCH demodulation performance
R4-167109

## Slide 2: Transmission signal pattern-1
        To test NPDCCH, the corresponding NPDSCH and NPUSCH format 2 for ACK/NACK, and the related scheduling delay need to be defined, i.e. transmission pattern for NPDCCH test.
          Do not configure DL-GapConfig-NB and DL-Bitmap-NB
        Transmit signal pattern within one period includes:
          NPDCCH
            Repetition level : as defined per test case
            Noise floor: Noc = [-98]dBm/15KHz
            Power level Ior: as defined in test such that Ior/Noc = SNR test point for NPDCCH

## Slide 3: Transmission signal pattern-2
        Transmit signal pattern within one period includes:
          4ms scheduling delay between end of NPDCCH and beginning of next NPDSCH
            OCNG pattern with duration 4ms
              Noise floor: Noc = [-98]dBm/15KHz
              Power level Ior: as defined in test such that Ior/Noc = SNR test point for NPDCCH
          NPDSCH
            Repetition level : 1
            Noise floor: Noc = [-98]dBm/15KHz
            Power level Ior: as defined in test such that Ior/Noc = SNR test point for NPDCCH

## Slide 4: Transmission signal pattern-3
        Transmit signal pattern within one period includes:
          12ms scheduling delay between end of NPDSCH and beginning of NPUSCH format 2
            OCNG pattern with duration of 11ms
              Noise floor: Noc = [-98]dBm/15KHz
              Power level Ior: as defined in test such that Ior/Noc = SNR test point for NPDCCH
            1ms switching time at the end of scheduling delay duration
              From downlink to uplink
              No external noise available
          NPUSCH format 2
            Repetition level : 1
            No external noise available
            Power level: define by RAN5
            Subcarrier spacing: 3.75KHz for extended coverage related tests and 15KHz for normal coverage related tests

## Slide 5: Transmission signal pattern-4
        Transmit signal pattern within one period includes:
          3ms interval between NPUSCH format 2 and the beginning of next NPDCCH transmission
            1ms switching time
              From uplink to downlink
              No external noise available
            OCNG pattern with duration 2ms
              Noise floor: Noc = [-98]dBm/15KHz
              Power level Ior: as defined in test such that Ior/Noc = SNR test point for NPDCCH