## Slide 1: 3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22 - 26 Aug, 2016
Huawei,HiSilicon,[Samsung],[Ericsson],[Qualcomm]…
Way forward on NB-IoT transmission signal pattern for NPDSCH demodulation performance
R4-167110

## Slide 2: Transmission signal pattern-1
        To test NPDSCH, the corresponding NPDCCH, NPUSCH format 2 and the related scheduling delay between transmitted signals need to be defined, i.e. transmission signal pattern for NPDSCH test.
          Do not configure DL-GapConfig-NB and DL-Bitmap-NB
        Transmit signal pattern within one period includes:
          NPDCCH
            Repetition level:[1,2,4 or 8];
            Noise floor: Noc0, i.e., no external noise
            Power level Ior: as defined in test such that Ior/Noc1 = SNR test point for NPDSCH

## Slide 3: Transmission signal pattern-2
        Transmit signal pattern within one period includes:
          1st 12ms scheduling delay between end of NPDCCH and beginning of the next NPDSCH
            OCNG pattern with duration 12ms
              Noise floor: Noc1 = [-93]dBm/15KHz
              Power level Ior: as defined in test such that Ior/Noc1 = SNR test point for NPDSCH
          NPDSCH
            Repetition level : as defined in the test case
            Noise floor: Noc1 = [-93]dBm/15KHz
            Power level Ior: as defined in test such that Ior/Noc1 = SNR test point for NPDSCH

## Slide 4: Transmission signal pattern-3
        Transmit signal pattern within one period includes:
          2nd 12ms scheduling delay between end of NPDSCH and beginning of the next NPUSCH format 2
            OCNG pattern with duration of 11ms
              Noise floor: Noc0 , i.e., no external noise
              Power level Ior: as defined in test such that Ior/Noc1 = SNR test point for NPDSCH
            1ms switching time at the end of scheduling delay duration
              From downlink to uplink
              No external noise available
          NPUSCH format 2
            Repetition level : 1
            No external noise available
            Power level: define by RAN5
            Subcarrier spacing: 3.75KHz for extended coverage related tests and 15KHz for normal coverage related tests

## Slide 5: Transmission signal pattern-4
        Transmit signal pattern within one period includes:
          3ms interval between end of NPUSCH format 2 and the beginning of the next NPDCCH transmission
            1ms switching time
              From uplink to downlink
              No external noise available
            OCNG pattern with duration 2ms
              Noise floor: Noc0 , i.e., no external noise
              Power level Ior: as defined in test such that Ior/Noc1 = SNR test point for NPDSCH