## Slide 1: WF on BS RF requirements impacts for shorten TTI feature
Ericsson, Huawei
3GPP TSG-RAN WG4 Meeting #81
Reno, USA, 14-18 Nov, 2016
Agenda Item: 10.1.3
Document for: Approval
R4-1610788

## Slide 2: Background
“Shorten TTI and processing time reduction” WI started in RAN4 #81
Potential impacts on BS RF requirements are discussed in R4-1609541 and R4-1609381.
This WF would capture RAN4#81 first agreements and list what should be further studied for next RAN4 meetings.

## Slide 3: Way Forward
The following BS RF requirements should not be impacted for support of shortened TTI :
  Bands, channel arrangement, channel bandwidth…
  Tx requirements:
    BS Output power
    Transmit ON/OFF power
    Unwanted emission
    Transmitted intermodulation
  All Rx requirements

## Slide 4: Way Forward
The following requirements should be further studied:
  Some definitions related to subframe need to be revisited for sTTI.
  Tx requirements:
    Output power dynamics
    Transmitted signal quality
      EVM/Time alignment error/Frequency error

## Slide 5: Overview of BS RF requirements impact
Type | Section | Requirements | Impacts
General | Bands and channel arrangement |  | No impact expected
Tx requirements | Output power |  | No impact expected
 | Output power dynamic | RE power control dynamic | To be further studied
 |  | Total power dynamic range | No impact expected
 |  | NB-IoT RB power dynamic range | No impact expected
 | Transmit ON/OFF | Transmitter OFF power | No impact expected
 |  | Transmitter transient period | No impact expected
 | Transmit signal quality | Frequency error | Measurement window ?
 |  | EVM | To be further studied
 |  | Time alignment error | To be further studied
 |  | DL RS power | No impact expected
 | Unwanted Emissions |  | No impact expected
 | Transmit Intermodulation |  | No impact expected
Rx requirements |  |  | No impact expected