## Slide 1: WF on NR general spurious emssion
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 #83 Meeting Hangzhou, China, 15 – 19 May, 2017
R4-1706072

## Slide 2: Background
MPR evaluations will start after the June meeting and each emission requirement needs to be fixed in advance.
For general spurious emission values in mmWave, there have been two proposals so far.
  -13 dBm/MHz (TRP)
    FCC limit
    Category A limit defined in the ITU-R SM.329-12
    ITU-R response in the SI phase.
  -30 dBm/MHz (TRP)
    Category B limit defined in the ITU-R SM.329-12
    (This might be required for NR in some countries)

## Slide 3: Way forward
It will be discussed how to specify NR general spurious emissions taking regions/countries where -30 dBm/MHz could be required in future into account in the next meeting.
Potential options are below.
  Option 1: Harmonic exceptions (like the current UE-to-UE co-existence requirement)
  Option 2: A-MPR with NS signaling
  Option 3: Implement analog filter (if feasible)
  Option 4: Extend measurement BW (if the bottleneck is narrow spurious)
  Option 5: Other