## Slide 1: 3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany, 21 – 25 Aug, 2017
Huawei,HiSilicon
Way forward on 8Rx simulation assumptions
R4-1708537

## Slide 2: Background
A new SI on LTE DL 8Rx antenna ports (RP-171491) was approved in RAN#76.
The work plan on 8Rx was approved in this meeting. Base on the work plan, the simulation assumptions should be agreed.

## Slide 3: Background-objectives
Evaluation of PDSCH demodulation performance with 8Rx for the transmission with rank lower than or equal to 4
Identify the scenarios for the evaluations
  Identify the necessary parameters including MCS, rank (≤4), antenna configuration and MIMO channel correlation, and propagation conditions
  Minimize the evaluation case numbers as much as possible
Run link level simulations, and compare 8Rx performance with 4Rx under the identified scenarios to investigate the performance gain
  Use MMSE-IRC as the reference receiver
Evaluation of PDSCH demodulation performance with 8Rx for the transmissions with rank higher than 4
Identify the scenarios for the evaluations
  Identify the necessary parameters including MCS, rank (>4), antenna configuration and MIMO channel correlation, and propagation conditions
  Minimize the evaluation case numbers as much as possible
Run link level simulations, and investigate the operating SNR for higher layer transmission
  Use MMSE-IRC as the reference receiver
Evaluation of PCFICH/PDCCH demodulation performance with 8Rx
Identify the scenarios for the evaluations
  Identify the necessary parameters including CCE levels, antenna configuration and MIMO channel correlation, and propagation conditions
  Minimize the evaluation case numbers as much as possible
Run link level simulations, and compare 8Rx performance with 4Rx performance under the identified scenarios to investigate the performance gain
  Use MMSE as the reference receiver
Based on the above evaluation results, identify the UE RF, RRM and UE performance requirements, which will be specified.
Identify the scope and objectives of UE RF requirements for 8Rx
  Decide the supported LTE bands for 8Rx
Identify the scope and objectives of RRM core requirements for 8Rx
Identify the scope and objectives of RRM performance requirements for 8Rx
Identify the scope and objectives of UE performance requirements for 8Rx
  UE demodulation requirements
  CSI requirements

## Slide 4: Simulation assumptions for PCFICH/PDCCH
Test number | Bandwidth | Aggregation level | Reference Channel | Propagation Condition | Antenna configuration and correlation Matrix
1 | 10 MHz | 8 CCE | R.15 FDD | ETU70 | 1x4 Low
2 | 10 MHz | 8 CCE | R.15 FDD | ETU70 | 1x8 Low
Table 4 simulation assumptions for PCFICH/PDCCH, 1Tx
Table 1 simulation assumptions for PCFICH/PDCCH, 1Tx
Table 2 simulation assumptions for PCFICH/PDCCH, 2Tx
Table 3 simulation assumptions for PCFICH/PDCCH, 4Tx
Test number | Bandwidth | Aggregation level | Reference Channel | Propagation Condition | Antenna configuration and correlation Matrix
1 | 10 MHz | 4 CCE | R.16 FDD | EVA70 | 2 x 4 Low
2 | 10 MHz | 4 CCE | R.16 FDD | EVA70 | 2 x 8 Low
Test number | Bandwidth | Aggregation level | Reference Channel | Propagation Condition | Antenna configuration and correlation Matrix
1 | 10 MHz | 2 CCE | R.17 FDD | EPA70 | 4 x 4 Low
2 | 10 MHz | 2 CCE | R.17 FDD | EPA70 | 4 x 8 Low

## Slide 5: Simulation assumptions for PDSCH, Rank≤4
Test number | Transmission mode | Bandwidth and MCS | Reference channel | Propagation condition | Correlation matrix and antenna config.
1 | TM3 | 10 MHz 16QAM,1/2 | R.11 FDD | EVA70 | 2x4 Low
2 | TM3 | 10 MHz 16QAM | R.11 FDD | EVA70 | 2x8 Low
Table 1 simulation assumptions for TM3 2 layer
Test number | Transmission mode | Bandwidth and MCS | Reference channel | Propagation condition | Correlation matrix and antenna config.
1 | TM4 | 10 MHz 16QAM,1/2 | R.74 FDD | EPA5 | 4x4 Low
2 | TM4 | 10 MHz 16QAM,1/2 | R.74 FDD | EPA5 | 4x8 Low
Table 2 simulation assumptions for TM4 4 layer

## Slide 6: Simulation assumptions for PDSCH, Rank>4
PDSCH | TM9 | 10MHz, 8x8 low, EPA5,rank5
 |  | 10MHz, 8x8 low, EPA5,rank6
 |  | 10MHz, 8x8 low, EPA5,rank7
 |  | 10MHz, 8x8 low, EPA5,rank8