## Slide 1: Finalization of IBB requirement for mmW
Qualcomm Incorporated
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711399
Document for approval
Agenda Item: 9.4.4.4.2

## Slide 2: Agreements from RAN 4 NR Ad Hoc #3 [1]:
To define IBB test for 50MHz, 100MHz, 200MHz and 400MHz channel BW
A single IBB test case should be defined for mmW with IBB jammer bandwidth same as wanted signal bandwidth
  In case of intra-band contiguous CA the jammer bandwidth is equal to the aggregated bandwidth
Jammer location:
  Two options were discussed: fixed or variable location (see appendix from [1])
Wanted signal and IBB Jammer levels
  It agreed to place jammer wanted level at REFSENS (EIS) + 14dB as for the ACS test
  Jammer level: it is agreed to place the jammer at REFSENS (EIS) + 44dB – SNR –IM
  SNR and IM values FFS

## Slide 3: Jammer location: background
The following two options were discussed [2]:
Fixed location
Variable location

## Slide 4: Jammer location: proposal
Proposal 1: to define a variable jammer location as specified in slide 3

## Slide 5: Jammer level: background
It is agreed to place the jammer at REFSENS (EIS) + 44dB – SNR –IM
SNR and IM values need to be decided

## Slide 6: Jammer level: proposal
Proposal 2: to place the jammer at
REFSENS + 44dB for bands n257, n258, n259
REFSENS + 43dB for band n260
Note: this means that SNR+IM = 0dB for the purpose of defining IBB requirements

## Slide 7: Summary of proposals
Proposal 1: to define a variable jammer location as specified in slide 3
Proposal 2: to place the jammer at
  REFSENS + 44dB for bands n257, n258, n259
  REFSENS + 43dB for band n260

## Slide 8: Draft table for IBB requirement
Rx Parameter | Units | Channel bandwidth |  |  | 
 |  | 50 MHz | 100 MHz | 200 MHz | 400 MHz
Power in Transmission Bandwidth Configuration | dBm | REFSENS + 14 dB |  |  | 
PInterferer | dBm | REFSENS + 44dB | REFSENS + 44dB | REFSENS + 44dB | REFSENS + 44dB
This requirement is applicable to bands n257, n258, n259 |  |  |  |  | 
PInterferer | dBm | REFSENS + 43dB | REFSENS + 43dB | REFSENS + 43dB | REFSENS + 43dB
This requirement is applicable to band n260 |  |  |  |  | 
BWInterferer | MHz | 50 | 100 | 200 | 400
FInterferer (offset) | MHz | 100 | 200 | 400 | 800
 |  | / | / | / | /
 |  | -100 | -200 | -400 | -800
FInterferer | MHz | FDL_low – 75 To FDL_high + 75 | FDL_low – 150 To FDL_high + 150 | FDL_low – 300 To FDL_high + 300 | FDL_low – 600 To FDL_high + 600

## Slide 9: References
[1] R4-1709962, “WF on UE IBB requirement for mmW”, Qualcomm Incorporated, Intel
[2] R4-1709748, “Proposal for IBB requirement for mmW”.
[3] R4-1708449, “On UE IBB requirement for mmW”, Qualcomm Incorporated.
[4] R4-1705478, “UE ACLR, ACS and IBB requirements for mmW”, Qualcomm Incorporated.