## Slide 1: WF on Transmit ON/OFF power and transient period
CATT, Huawei, …
3GPP TSG-RAN WG4 Meeting #84bis R4-1711799
Dubrovnik, Croatia, 9th – 13st Oct, 2017
Agenda Item: 8.27.3.2

## Slide 2: Background
There are some discussions about the OTA transmit ON/OFF power and transient period based on the following papers:
  [1] R4-1711115_Tx ON/OFF requirements and transients Huawei
  [2] R4-1710813_OTA transmitter OFF power requirement for TDD Ericsson
  [3] R4-1710466_Discussion on transmit ON/OFF power CATT
  [4] R4-1711116_TP to TR 37.843 - Tx ON-OFF requirements Huawei

## Slide 3: Agreement for OFF power
Following agreements have been reached:
  OTA Transmit OFF power is a co-location requirement
    The requirement is defined at the co-location reference antenna conductive output side.
  For UTRA, the output power at the co-location reference antenna shall be less than ：-85dBm/MHz – 30dB + X dB
  For E-UTRA, the output power at the co-location reference antenna shall be less than ：- 85dBm/MHz – 30dB + X dB
where X is a scaling factor. There are two options for how to determine X:
  X = 9 dB for E-UTRA and 6 dB for UTRA.
  X = 10log10(M) where M is the number of transceivers in the AAS BS.

## Slide 4: Agreement for transient period
  The conductive on/off transient period could be reused for OTA requirement.
ON to OFF | Transient period length [us]
OFF to ON | 17
ON to OFF | 17

## Slide 5: WF
Companies are encouraged to provide paper in the next meeting about which option in slide 3 should be used to determine scaling factor ‘X’ .