## Slide 1: Way forward for CRS-IM related advanced receiver impact analysis for network-based CRS-IM
Ericsson
3GPP TSG-RAN WG4 Meeting #85 Reno, USA, Nov. 27 – Dec. 1 2017
R4-1713897

## Slide 2: RAN4 observations
For legacy UEs with CRS-IM, RAN4 has the following observations:
  Legacy UEs with CRS-IM receivers are unaware on neighbouring cell CRS muting and perform CRS-IM receive processing under assumption that neighbouring cell CRS signals are present
  CRS-IC with muted BW CRS in aggressor cell has performance impact compared with CRS-IC with full BW CRS in aggressor cell
    The impact is implementation dependent and scenario dependent.
      Some companies observed 1~2 dB degradation at least for some scenarios
      Some companies observed negligible performance degradation
It is beneficial for UE to get network assistance on the CRS muting in the neighbouring cells for advanced receivers

## Slide 3: RAN4 observations
Impact to CCIM Type A/B receivers
  Neighboring cell CRS muting has limited impact on the CCIM receivers performance under practical conditions.
Impact on NAICs
  For legacy NAIC UE, some degradation may be expected

## Slide 4: RAN4 conclusions
As a conclusion of the analysis of Objective #1 and Objctive #2 of the WID (RP-171408), RAN4 sees beneficial for UE to be aware of whether neighbouring cells use CRS muting or not
Solutions on how to handle impact to legacy and Rel-15 UEs are FFS