## Slide 1: Way forward on UE TA offset for FDD and TDD in NR
NTT DOCOMO
3GPP TSG-RAN WG4 #86 Meeting
Athens, Greece, February 26th - March 2nd, 2018
R4-1802031
Document for: Approval
Agenda item: 7.9.8.1

## Slide 2: Background
TS38.133 7.1.2 (UE transmit timing requirements):
TS38.211:
The specification is described without defining duplex modes, i.e., without differentiation between FDD and TDD.
Observation: NR UE needs to differentiate UL transmit timing on FDD cell and that on TDD cell as well as in LTE.

## Slide 3: Background
Issue in LTE FDD-TDD UL CA
  TS36.213 4.2.3 (Transmission timing adjustment)
Observation: In LTE, due to different NTA offset value between FDD and TDD, TA handling at network and at UE are complicated when TDD-FDD UL CA is introduced

## Slide 4: Background
Issue in LTE FDD-TDD UL CA
  Example#1: FDD PCell and TDD SCell
    UE applies PCell UL transmit timing on SCell (i.e., follows NTA with NTA offset = 0 even on TDD cell)
    Network needs to signal NTA on FDD PCell so that NTA >= NTA offset (624)
      NTA for each of all other UEs also needs to be adjusted due to the FDD-TDD UL UE
  Example#2: TDD PCell and FDD SCell
    UE applies PCell UL transmit timing on Scell (i.e., follows NTA with NTA offset = 624 even on FDD cell)
    For other UEs on FDD SCell, network needs to signal NTA so that UL reception timings are aligned between TDD-FDD UL CA UE and other UEs
FDD DL (RX)
TDD DL (RX)
NTA offset
NTA
FDD UL (TX)
TDD UL (TX)
FDD DL (TX)
TDD DL (TX)

## Slide 5: Discussion
Possible alternative solution:
  Apply same NTA offset value between FDD and TDD within the same frequency range
    As in R4-1801416, RAN1 recommends that NTA offset is the same with and without NR-LTE co-existence for TDD in FR1
Frequency range and band of cell used for uplink transmission | NTA offset
FR1 except for LTE-NR coexistence bands | 25560
FR1 LTE-NR coexistence bands (FDD) | FFS (need to check with RAN1)
FR1 LTE-NR coexistence bands (TDD) | 25560
FR2 | 13763
Observations:
Irrespective of FDD UL CA, TDD UL CA and TDD-FDD UL CA, TA handling at network and at UE could be unified in each frequency range by this alternative solution
For FDD LTE-NR coexistence bands, difference between NTA offset of LTE UE and that of NR UE will be relatively large compared with TDD LTE-NR coexistence case.

## Slide 6: Proposal
Apply same NTA offset value between FDD and TDD within the same frequency range
  Table 7.1.2-2 in TS38.133 is updated as below
Send LS to RAN1 to ask whether or not NTA offset can be the same with and without NR-LTE co-existence for FDD in FR1
Frequency range and band of cell used for uplink transmission | NTA offset
FR1 | 25560
FR2 | 13763