## Slide 1: WF on inter-RAT SFTD measurement without gaps for EN-DC capable UE
Ericsson, NTT DoCoMo, ZTE Corporation, MediaTek, Nokia, Nokia Shanghai Bell, LG Electronics
R4-1803156
3GPP RAN WG4 Radio #86
Athens, Greece, February 26 – March 2, 2018

## Slide 2: Background
The use case presented by operator concerns timing drift between LTE system and NR system
Timing drift between the LTE system and the NR system may lead to outdated information on the timing offset between an LTE PCell and NR neighbor cells
Knowledge about the timing offset is needed in order for the LTE PCell to configure measurement gaps for NR inter-RAT measurements
See further agreements from RAN4 AH-1801 (R4-1801296). The present WF covers details only for one out of two agreed execution models.

## Slide 3: Agreements Inter-RAT SFTD measurement without gaps
Core requirements are specified for SINR ≥ -3dB
Inter-RAT SFTD measurement configuration comprises
  SSB frequency location
  SSB SCS
  SMTC periodicity
  SMTC window duration
  Optional: PCID
Inter-RAT SFTD measurement reporting comprises
  PCID
  SFTD result
  Optional: RSRP
  Success/failure indication
The UE reports up to 3 strongest cells it reliably detects
UE may cause interruptions at onset and end of the complete inter-RAT SFTD measurement
  Interruption length depends on UE RF capabilities (e.g. utilizes separate NR receiver, or changes bandwidth of common receiver)
  When interruptions are allowed is FFS

## Slide 4: For RAN4#86bis Inter-RAT SFTD measurement without gaps
Companies are encouraged to provide:
Measurement reporting delay under side condition SINR ≥ -3dB, for
  FR1
  FR2
Analysis on how to handle the scenario EN-DC combination with MSD, i.e., where simultaneous LTE PCell Tx and NR carrier Rx is unfeasible