## Slide 1: Way forward on V2X RF Maintenance
QC, HW, LGE, Harman Samsung
3GPP TSG-RAN WG4 Meeting #86 R4-1803355
Athens, Greece, Feb 26th– Mar 2nd, 2018
Agenda Item: 5.7

## Slide 2: IBE
Agreement
  Specify in-band emission requirement without considering IMD exceptions and apply MPR for IMD product.
  For intra-band contiguous multi-carrier operation the in-band emission requirement (General, IQ Image or Carrier leakage) of each channel is calculated separately as Pgeneral, PSSCH,c(i), PIQ, PSSCH,c(i), PLO, PSSCH,c(i), Pgeneral, PSCCH,c(i), PIQ, PSCCH,c(i), PLO, PSCCH,c(i) for each carrier respectively according to subcaluse 6.5.2A.3. In-band emissions combined limit for the aggregated bandwidth is evaluated in each non-allocated RB. For each such RB, the minimum requirement is calculated as the PsumIBE.CA, where PsumIBE.CA is the linear sum of Pgeneral, PSSCH,c(i), PIQ, PSSCH,c(i), PLO, PSSCH,c(i), Pgeneral, PSCCH,c(i), PIQ, PSCCH,c(i), PLO, PSCCH,c(i) for all carriers.
  This will be added as NOTEs in tables 6.5.2A.3.1-1 and Table 6.5.2A.3.1-2
  further study to needed MPR to supress the in channel IMD peaks for 2 carriers V2X CA waveforms with non-adjacent control and data clusters in each carrier.

## Slide 3: A-MPR (and A-SEM, A-SE)
Working assumption
  The UE is required to declare (at least 1) expected post-antenna connector gain (external antenna gain – cable loss between the UE antenna connector and external antenna) for external antenna case.
  The existing A-SE and A-SEM is in eirp. Conducted emission mask is obtained by subtracting the expected post-antenna connector gain.
  Need A-MPR analysis for post-antenna connector gain 0, 1, …, 7 dB for external antenna case.
  [information] A-MPR for larger post antenna connector gain should accommodate more stringent conducted emission requirement
FFS system impact.