## Slide 1: Way forward on higher velocity UE RRM requirements
Huawei, HiSilicon, Ericsson, Nokia, Nokia Shanghai Bell…
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26th February – 2nd March, 2018
Agenda item: 6.19.4.1
R4-1803487

## Slide 2: Background
We have reached the following agreements in RAN4 #85:
  For non-DRX requirements with gap pattern #0 and for intra-frequency measurement
    Reuse Rel-13 cell identification and measurement delay requirements in high Doppler channel up to 220Hz Doppler spread.
    Reuse Rel-13/14 measurement accuracy requirements in high Doppler channel up to 220Hz Doppler spread.
  FFS for inter-frequency measurement requirements
  FFS for RRM requirements with DRX

## Slide 3: Way forward
  On gap sharing and higher-velocity operation
    Introduce a new measurement gap sharing table for eFeMTC UEs operating under higher velocity, and the values of the table are FFS.
    Inter-frequency requirements under higher-velocity operation are FFS.
    If higher-velocity indication is received by the efeMTC UE, the UE shall use the measurement gap sharing table associated with higher-velocity.